## Slide 1
LESSON 01
Introduction and Setup
MCU architecture | The hardware | GitHub and SSH
Embedded Software Development in C/C++
Gamma Intelligence | 100 academic hours | 25 sessions

## Slide 2
Today
Lesson 01 | Introduction and Setup
2
Part 1
MCU architecture
What is inside a chip
RISC-V and Cortex-M
Part 2
The boards
Three platforms
What you pay for
Part 3
GitHub account
SSH keys
First clone
Before you leave today
Your GitHub username must be written down on the shared list. Without it you cannot clone the repository next session.

## Slide 3
PART 1
MCU Architecture
What a microcontroller is, and what it is not

## Slide 4
Three Kinds of Computer
Lesson 01 | Introduction and Setup
4
 | Desktop PC | Application CPU | Microcontroller
Example | Intel Core i7 | Raspberry Pi 5 | ESP32-C3
RAM | 16-64 GB external | 4-8 GB external | 400 KB on-chip
Storage | SSD, terabytes | SD card, GB | Flash, a few MB
Operating system | Windows, Linux | Linux | None, or a small RTOS
Boot time | Tens of seconds | Seconds | Milliseconds
Power | Tens of watts | Watts | Milliwatts
Your code is | One process | One process | The whole system
The key difference
On a PC the operating system stands between your code and the hardware. Here there is nothing in between.

## Slide 5
Inside the Chip
Lesson 01 | Introduction and Setup
5
CPU Core
Fetches and executes instructions. One core, sometimes two.
Memory
Flash holds the program. SRAM holds the variables.
Peripherals
GPIO, timers, ADC, UART, I2C, SPI. Hardware blocks, not software.
Bus
Connects everything. Peripherals are just addresses in memory.
The central idea
A peripheral is controlled by writing to a register, and a register is a memory address. Everything reduces to reading and writing memory.

## Slide 6
Memory: Where Things Live
Lesson 01 | Introduction and Setup
6
Region | Typical size | Survives reset | Holds
Flash | 1-16 MB | Yes | Program code, constants
SRAM | 20-520 KB | No | Variables, stack, heap
Registers | Bytes | No | Peripheral control and status
EEPROM / NVS | KB | Yes | Settings, calibration
SRAM is the scarce resource. 400 KB sounds like a lot until you allocate a display buffer.
There is no virtual memory and no memory protection by default. A bad pointer corrupts whatever it points at.
The stack and the heap grow toward each other. When they meet, the symptom is not an error message.

## Slide 7
What Happens at Power-On
Lesson 01 | Introduction and Setup
7
1. Power stabilises, the reset line releases
2. The core reads the reset vector from a fixed address in flash
3. A startup routine sets up the stack pointer
4. Initialised globals are copied from flash into SRAM
5. Uninitialised globals are zeroed
6. C++ static constructors run
7. main() is called - and only now does your code appear to start
Why this matters
Steps 3 to 6 happen before main(). A bug there produces a board that appears dead with no output at all.

## Slide 8
Instruction Sets
Lesson 01 | Introduction and Setup
8
The instruction set is the contract between the compiler and the silicon.
CISC (x86): many complex instructions, variable length. Optimised for code density in an era when memory was expensive.
RISC (ARM, RISC-V): fewer, simpler, fixed-length instructions. Easier to pipeline, easier to build, easier to verify.
Every chip in this course is RISC. The difference between them is which RISC.
 | ARM Cortex-M | RISC-V
Owner | ARM Ltd, licensed | Open standard, royalty free
Ecosystem | Mature, huge toolchain support | Younger, growing fast
In this course | STM32, RP2350 | ESP32-C3, RP2350

## Slide 9
PART 2
The Hardware
Three boards, three answers to the same problem

## Slide 10
Three Boards on the Table
Lesson 01 | Introduction and Setup
10
ESP32-C3
RISC-V, WiFi and BLE built in.
Thumbnail sized.
Our reference platform.
STM32 NUCLEO
Cortex-M4, industrial workhorse.
Debugger on the board.
What you meet at work.
RP2350
Cortex-M33 AND RISC-V on one die.
Boots into either.
Programmable IO.
Look at the RP2350 again
One piece of silicon carrying two different instruction sets, selected at boot. That is not a normal thing for a chip to do.

## Slide 11
Side by Side
Lesson 01 | Introduction and Setup
11
 | ESP32-C3 | STM32F401 | RP2350
Core | RISC-V | Cortex-M4 | M33 or RISC-V
Clock | 160 MHz | 84 MHz | 150 MHz
SRAM | 400 KB | 96 KB | 520 KB
Wireless | WiFi + BLE | None | None
On-board debugger | No | Yes, ST-Link | No
Special feature | Cheap and connected | Ecosystem and tooling | PIO state machines
Rough price | Very low | Moderate | Low
There is no best board
Only the board that fits the constraint you have: cost, power, connectivity, certification.

## Slide 12
What You Pay For
Lesson 01 | Introduction and Setup
12
The MCU itself is often the cheapest part of the board.
USB to serial converter - so a PC can talk to the chip.
Voltage regulators - the chip wants 3.3V, USB gives 5V.
Crystal oscillator - an accurate clock reference.
On-board debugger - lets you stop the CPU and inspect it. This is the expensive one.
Headers, protection, decoupling - the parts nobody thinks about until they are missing.
The NUCLEO premium
The ST-Link on the NUCLEO is why it costs more than the ESP32-C3. You are buying a debugger, not a faster chip.

## Slide 13
PART 3
GitHub and SSH
Setting up how you will hand in every assignment

## Slide 14
Why Version Control
Lesson 01 | Introduction and Setup
14
Firmware development is a long sequence of small changes, most of which do not work.
Git lets you go back to the last version that did.
It is also how you will submit homework in this course.
And it is the single most universally expected skill in the job you are training for.
commit
Save a checkpoint
push
Send it to GitHub
clone
Get a copy on a new machine

## Slide 15
Generating an SSH Key
Lesson 01 | Introduction and Setup
15
ssh-keygen -t ed25519 -C "your.email@example.com"
# Press Enter to accept the default location.
# A passphrase is optional but recommended.
# Show the PUBLIC key - this is the one you paste
cat ~/.ssh/id_ed25519.pub
# Then: github.com -> Settings -> SSH and GPG keys
# -> New SSH key -> paste -> Add
Use ed25519, not RSA. Shorter, safer, and it keeps us all on the same commands.
The .pub file is public and safe to share.
The file without .pub is private. It never leaves your machine.
Never paste the private key anywhere

## Slide 16
If It Does Not Work
Lesson 01 | Introduction and Setup
16
# Windows: ssh-agent is disabled by default.
# Run PowerShell as Administrator:
Set-Service ssh-agent -StartupType Automatic
Start-Service ssh-agent
# Everyone: verify the connection
ssh -T git@github.com
# First run asks about a fingerprint. Type: yes
# Success looks like:
# Hi <username>! You have successfully
# authenticated...
The ssh-agent service is the most common failure on Windows.
The fingerprint prompt is normal, not an attack.
ssh -T is a test, not a login. It is supposed to refuse a shell.

## Slide 17
Identity and Fallback
Lesson 01 | Introduction and Setup
17
git config --global user.name "Your Name"
git config --global user.email "same@as.github"
The email MUST match your GitHub account, or commits will not be linked to you
If SSH refuses to cooperate today
Use HTTPS with a Personal Access Token instead: GitHub -> Settings -> Developer settings -> Personal access tokens -> Fine-grained tokens. Select the course repository, grant Contents read and write, and use the token as your password when git asks. You leave with a working clone either way; SSH can be fixed at home.

## Slide 18
Summary
Lesson 01 | Introduction and Setup
18
A microcontroller runs your code directly on the hardware, with no operating system underneath it.
Peripherals are controlled through registers, and registers are memory addresses.
Flash holds the program, SRAM holds the data, and SRAM is the resource you will run out of first.
Our three boards are three different trade-offs, not three quality levels.
Git and SSH are set up now because every assignment from here on is submitted through them.
Homework
Finish your SSH setup if it is not working yet. Clone the course repository and confirm you can push a change to the file with your name in it. Bring a working laptop to the next session - we install PlatformIO and flash the first firmware.