## Slide 1
LESSON 02
First Firmware
PlatformIO | Blink and button | git workflow
Embedded Software Development in C/C++
Gamma Intelligence | ESP32-C3 Super Mini

## Slide 2
Today
Lesson 02 | First Firmware
2
Part 1
VS Code + PlatformIO
Install the toolchain
Project anatomy
platformio.ini
Part 2
Build, upload, monitor
Blink on GPIO 8
Serial output
Read the BOOT button
Part 3
git add, commit, push
Commit messages
What to do when
git refuses
By the end of today
Firmware you wrote is running on your board, and the source code is on GitHub.

## Slide 3
PART 1
VS Code and PlatformIO
The tools you will use every single session

## Slide 4
Who Does What
Lesson 02 | First Firmware
4
VS Code
The editor.
Where you read and write code.
Knows nothing about microcontrollers by itself.
PlatformIO
The build system.
Downloads the compiler, builds the firmware, uploads it, opens the serial monitor.
Toolchain
Compiler + linker + upload tool for a specific chip.
Installed per platform, automatically, on first build.
One environment for the whole course
ESP32-C3, STM32 and RP2350 are all driven from the same PlatformIO setup.

## Slide 5
Installing PlatformIO
Lesson 02 | First Firmware
5
Install VS Code from code.visualstudio.com
Extensions (Ctrl+Shift+X) -> search "PlatformIO IDE" -> Install
Wait for "PlatformIO Core installed" - the alien head icon appears in the sidebar
Restart VS Code once if the icon does not appear
The first build is slow - that is normal
PlatformIO downloads the whole ESP32 toolchain (~1 GB) on the first build. On classroom WiFi this takes minutes. Start it, let it run, do not cancel.

## Slide 6
Project Anatomy
Lesson 02 | First Firmware
6
lesson-02/
platformio.ini <- the project definition
src/
main.cpp <- your code lives here
include/ <- your headers (.h)
lib/ <- project-local libraries
.pio/ <- build output. Generated.
Never edit, never commit.
One folder = one project = one platformio.ini
PlatformIO: Home -> New Project, or clone one that already exists
A project is text files
Everything that matters is main.cpp plus platformio.ini. That is why the whole project goes into git and builds identically on any machine.

## Slide 7
platformio.ini
Lesson 02 | First Firmware
7
[env:lolin_c3_mini]
platform = espressif32
board = lolin_c3_mini
framework = arduino
monitor_speed = 115200
platform: which chip family and toolchain
board: our ESP32-C3 Super Mini
framework: the API our code is written against
monitor_speed: must match Serial.begin()
Five lines, three sources of silent failure
Wrong board id -> firmware for the wrong chip. Wrong monitor_speed -> garbage in the serial monitor. Wrong framework -> nothing compiles.

## Slide 8
Build, Upload, Monitor
Lesson 02 | First Firmware
8
Build
Check mark in the status bar.
Compiles and links.
Errors appear here first.
Upload
Right arrow in the status bar.
Builds, then flashes over USB.
Monitor
Plug icon in the status bar.
Shows Serial output.
Exit: Ctrl+C in the terminal.
Upload fails or the port is missing?
1) Close the serial monitor - it holds the port. 2) Check the USB cable - charge-only cables have no data lines. 3) Try the other USB connector on the board.

## Slide 9
PART 2
Blink, Serial, Button
The smallest programs that prove the whole chain works

## Slide 10
Blink
Lesson 02 | First Firmware
10
#include <Arduino.h>
static const uint8_t LED_PIN = 8U;
static const uint32_t BLINK_MS = 500U;
void setup() {
pinMode(LED_PIN, OUTPUT);
}
void loop() {
digitalWrite(LED_PIN, LOW); // ON
delay(BLINK_MS);
digitalWrite(LED_PIN, HIGH); // OFF
delay(BLINK_MS);
}
setup() runs once at boot
loop() runs forever after it
LED_PIN and BLINK_MS: named constants at the top, no magic numbers below
uint8_t / uint32_t: fixed-width types, always

## Slide 11
Why LOW Means ON
Lesson 02 | First Firmware
11
The blue status LED on this board sits between 3.3V and GPIO 8
The GPIO pin is on the cathode side and sinks current
Pin LOW -> current flows -> LED on. Pin HIGH -> no current -> LED off
This is called active-low, and it is everywhere in embedded: buttons, resets, chip-select lines
GPIO 8 is also a strapping pin
It must be HIGH at reset for normal boot - the board's own pull-up takes care of that. Later, when we hang external hardware on pins, GPIO 2, 8 and 9 are the ones to treat with care.

## Slide 12
Serial: Your First Debugging Tool
Lesson 02 | First Firmware
12
void setup() {
Serial.begin(115200U);
pinMode(LED_PIN, OUTPUT);
}
void loop() {
digitalWrite(LED_PIN, LOW);
Serial.println("LED on");
delay(BLINK_MS);
digitalWrite(LED_PIN, HIGH);
Serial.println("LED off");
delay(BLINK_MS);
}
115200 here = monitor_speed there
println is how firmware talks back
When something misbehaves, the first question is always: what does Serial say?

## Slide 13
Reading a Button
Lesson 02 | First Firmware
13
static const uint8_t BUTTON_PIN = 9U; // BOOT
void setup() {
pinMode(BUTTON_PIN, INPUT_PULLUP);
pinMode(LED_PIN, OUTPUT);
}
void loop() {
if (digitalRead(BUTTON_PIN) == LOW) {
digitalWrite(LED_PIN, LOW); // pressed
} else {
digitalWrite(LED_PIN, HIGH); // released
}
}
The board has two buttons: RESET restarts the chip, BOOT sits on GPIO 9
After boot, BOOT is just a button: pressed connects the pin to ground, so pressed reads LOW - active-low again
But GPIO 9 is a strapping pin: held LOW during reset it enters the serial bootloader. Do not hold it while resetting
No delay() here: loop() polls the pin thousands of times per second

## Slide 14
PART 3
The git Workflow
How every assignment in this course is handed in

## Slide 15
add, commit, push
Lesson 02 | First Firmware
15
cd embedded-cpp-2026-autumn
git pull # start current
# ... edit code ...
git status # what changed?
git add lesson-02/
git commit -m "lesson-02: blink with button"
git push
pull first, push last
Commit messages: English, ASCII, say what the change is
Commit when something works, not once at midnight
Never commit .pio/
Build output is generated, huge, and machine-specific. The .gitignore in the course repository already excludes it - do not force-add it.

## Slide 16
When git Refuses
Lesson 02 | First Firmware
16
It says | It means | You do
rejected: fetch first | GitHub has commits you do not | git pull, then push again
merge conflict | Same lines changed twice | Edit the marked file, add, commit
Permission denied (publickey) | SSH key problem from lesson 01 | ssh -T git@github.com to test
not a git repository | You are in the wrong folder | cd into the cloned repository
Read the message before asking
git error messages usually contain the fix. Reading them is a course skill, same as reading a datasheet.

## Slide 17
Summary
Lesson 02 | First Firmware
17
PlatformIO turns VS Code into the whole embedded toolchain: build, upload, monitor
A project is platformio.ini plus src/ - everything else is generated
Blink proves the chain: compiler -> USB -> flash -> running code
The blue LED (GPIO 8) and the BOOT button (GPIO 9) are both active-low
Work flows through git: pull, edit, add, commit, push
Homework
Make the LED blink a morse-style pattern and control it with the button - scaffold in lesson-02/homework. Commit and push before the next session.