## Slide 1
LESSON 08
Structs, Classes and PWM
From eight colours to sixteen million
Embedded Software Development in C/C++
ESP32-C3 Super Mini | Session 8 of 25

## Slide 2
Today
Lesson 08 | Structs, Classes and PWM
2
Structs: values that belong together travel together
The first class: an object that owns three pins
PWM: how a digital pin produces something between on and off
Then PWM moves inside the class, and nothing outside it changes
Goal
By the end of the lesson your LED can show any colour, and the code that asks for a colour does not know how the LED works.

## Slide 3
PART 1
Structs
One name for several values

## Slide 4
Three numbers that belong together
Lesson 08 | Structs, Classes and PWM
4
struct Colour {
uint8_t red;
uint8_t green;
uint8_t blue;
};
Colour warm = { 255U, 120U, 0U };
Serial.println(warm.red); // 255
An array holds many of one thing
A struct holds a few different things
Each field has its own name and type
The dot reaches a field

## Slide 5
A struct is a value, not a pointer
Lesson 08 | Structs, Classes and PWM
5
Colour a = { 10U, 20U, 30U };
Colour b = a; // b is a separate copy
b.red = 99U; // a.red is still 10
void show(const Colour *c); // no copy, and read only
Colour dim(Colour c); // takes a copy, returns a new one
Three bytes are cheap to copy
For a small struct, passing a copy is fine and safer. For a big one, pass a pointer. The rule is the same as for any other value.

## Slide 6
PART 2
The First Class
A struct that can also do things

## Slide 7
A class: data plus behaviour
Lesson 08 | Structs, Classes and PWM
7
class RgbLed {
public:
RgbLed(uint8_t red, uint8_t green, uint8_t blue);
void begin(void);
void setColour(Colour c);
private:
uint8_t m_red;
uint8_t m_green;
uint8_t m_blue;
};
public: what others may use
private: what only the class touches
m_ marks a field, so a local never hides one

## Slide 8
The constructor runs at birth
Lesson 08 | Structs, Classes and PWM
8
RgbLed::RgbLed(uint8_t red, uint8_t green, uint8_t blue)
: m_red(red), m_green(green), m_blue(blue) {
}
void RgbLed::begin(void) {
pinMode(m_red, OUTPUT);
pinMode(m_green, OUTPUT);
pinMode(m_blue, OUTPUT);
}
Why begin() and not the constructor
An object made before setup() runs exists before the chip is ready. Remember the pins in the constructor, touch the hardware in begin().

## Slide 9
Using the object
Lesson 08 | Structs, Classes and PWM
9
static const Colour RED = { 255U, 0U, 0U };
RgbLed led(PIN_RED, PIN_GREEN, PIN_BLUE);
void setup(void) {
led.begin();
led.setColour(RED);
}
One object, one LED
A second LED is a second object, same class
led.m_red is not allowed: it is private

## Slide 10
PART 3
PWM
Between on and off, very fast

## Slide 11
A pin has two states, and no middle
Lesson 08 | Structs, Classes and PWM
11
digitalWrite can only give 0 V or 3.3 V
So the pin is switched on and off thousands of times a second
The eye cannot follow that; it averages what it sees
The share of time spent on is called the duty cycle
Duty | The pin | The eye
0 | always off | dark
64 | on a quarter of the time | dim
128 | on half the time | medium
255 | always on | full

## Slide 12
Two settings to choose
Lesson 08 | Structs, Classes and PWM
12
Setting | We use | Why
Frequency | 5000 Hz | slower starts to flicker, especially at the edge of vision
Resolution | 8 bits | 256 steps, and a step fits in a uint8_t
Largest duty | 255 | (1 << 8) - 1, the same edge as always
More bits are not always better
Frequency and resolution share the same timer. Ask for both too high and the chip cannot deliver. For an LED, 8 bits at 5 kHz is comfortable.

## Slide 13
PWM on the ESP32-C3
Lesson 08 | Structs, Classes and PWM
13
static const uint32_t PWM_FREQ_HZ = 5000U;
static const uint8_t PWM_BITS = 8U;
static const uint8_t CHANNEL_RED = 0U;
ledcSetup(CHANNEL_RED, PWM_FREQ_HZ, PWM_BITS); // once, in begin()
ledcAttachPin(PIN_RED, CHANNEL_RED); // once, in begin()
ledcWrite(CHANNEL_RED, 128U); // any time after that
PWM is made by a channel, not by a pin; the chip has six of them
ledcAttachPin connects a pin to a channel; ledcWrite talks to the channel

## Slide 14
Our LED counts backwards
Lesson 08 | Structs, Classes and PWM
14
static const uint8_t PWM_MAX = 255U;
// common anode: the pin sinks the current
// 0 is full brightness, 255 is off
ledcWrite(CHANNEL_RED, PWM_MAX - c.red);
The first thing that will go wrong
Ask for red and get cyan, ask for black and get white. One subtraction, in one place inside the class, and every caller is spared it.

## Slide 15
PART 4
Sixteen Million Colours
The class changes inside, the calls do not

## Slide 16
Same class, new insides
Lesson 08 | Structs, Classes and PWM
16
void RgbLed::setColour(Colour c) {
ledcWrite(CHANNEL_RED, PWM_MAX - c.red);
ledcWrite(CHANNEL_GREEN, PWM_MAX - c.green);
ledcWrite(CHANNEL_BLUE, PWM_MAX - c.blue);
}
led.setColour(warm); // this line never changed
That is what the class bought you
digitalWrite became ledcWrite, eight colours became millions, and not one line outside the class had to be touched.

## Slide 17
Mixing by numbers
Lesson 08 | Structs, Classes and PWM
17
Colour | red | green | blue
Red | 255 | 0 | 0
Orange | 255 | 120 | 0
Yellow | 255 | 255 | 0
White | 255 | 255 | 255
Dim white | 40 | 40 | 40
256 x 256 x 256 combinations, and no new wiring
Green looks brighter than red at the same number: the eye, not a bug

## Slide 18
Tonight: the colour wheel
Lesson 08 | Structs, Classes and PWM
18
Walk the colours in a circle: red -> yellow -> green -> cyan -> blue -> magenta -> red
One number decides where you are on that circle: the hue, 0 to 359
The potentiometer sets that number, so the knob picks the colour
Turning the knob a full turn walks the whole wheel
Everything you need, you now have
A struct to carry a colour, a class to drive the LED, PWM to make the shades, and the knob you already know how to read.

## Slide 19
Summary
Lesson 08 | Structs, Classes and PWM
19
A struct groups values; a class adds what can be done with them
private keeps the inside of an object the owner's business
The constructor remembers, begin() touches the hardware
PWM turns a two-state pin into 256 levels of brightness
Homework
Build the colour wheel: the knob picks the hue, the LED shows it. Details are in homework/README.md.