## Slide 1
LESSON 09
References and Overloading
And why two buttons need two objects
Embedded Software Development in C/C++
ESP32-C3 Super Mini | Session 9 of 25

## Slide 2
Today
Lesson 09 | References, Overloading and a Button Class
2
References: a second name for a variable that already exists
Overloading: one name, several versions, chosen by the arguments
A second button, and the moment static stops being enough
A Button class: every object remembers for itself
Goal
By the end of the lesson two buttons work side by side without disturbing each other, and you have the parts for a two-player game.

## Slide 3
PART 1
References
Another name for the same box

## Slide 4
A second name for the same box
Lesson 09 | References, Overloading and a Button Class
4
uint8_t count = 5U;
uint8_t &alias = count; // alias is another name for count
alias = 7U; // count is now 7
No new box is made: alias and count are the same memory
It must be tied to something when it is created
Once tied, it can never point anywhere else

## Slide 5
Three ways to hand over a value
Lesson 09 | References, Overloading and a Button Class
5
 | Copy | Pointer | Reference
Declared as | Colour c | Colour *c | Colour &c
Called as | f(x) | f(&x) | f(x)
Can change x | no | yes | yes
Can be empty | no | yes, nullptr | no
Fields reached with | c.red | c->red | c.red
A reference is a pointer that behaves
It does the same job as a pointer, but it cannot be empty, cannot be moved, and needs no & or * at the call.

## Slide 6
The one you will use most
Lesson 09 | References, Overloading and a Button Class
6
void setColour(const Colour &c); // no copy, read only
led.setColour(warm); // called like a copy
& : the function works on the original, nothing is copied
const : and it promises not to change it
At the call it looks exactly like passing a copy
The default for anything bigger than a number
Fast like a pointer, safe like a copy. For a single uint8_t, a plain copy is still fine.

## Slide 7
PART 2
Overloading
One name, several versions

## Slide 8
Same name, different inputs
Lesson 09 | References, Overloading and a Button Class
8
void setColour(const Colour &c);
void setColour(uint8_t red, uint8_t green, uint8_t blue);
led.setColour(warm); // the first one
led.setColour(255U, 120U, 0U); // the second one
The compiler picks by the number and the types of the arguments
The caller uses whichever form is handier at that moment
In C this would need two names: setColour and setColourRgb

## Slide 9
Write the work once
Lesson 09 | References, Overloading and a Button Class
9
void RgbLed::setColour(uint8_t red, uint8_t green, uint8_t blue) {
const Colour c = { red, green, blue };
setColour(c); // hand over to the other one
}
One version does the real work; the others only translate
A bug fixed there is fixed for every form
Return type alone is not enough
uint8_t read() and int16_t read() cannot live together: the call read() looks the same for both. The parameters have to differ.

## Slide 10
PART 3
Two Buttons
Where static stops being enough

## Slide 11
Wiring the second button
Lesson 09 | References, Overloading and a Button Class
11
Part | Connects to
Button A, player 1 | GPIO 0 and GND
Button B, player 2 | GPIO 1 and GND
RGB LED | GPIO 5, 6, 7 as before, common anode to 3V3
Both buttons use INPUT_PULLUP
No resistors. Not pressed reads HIGH, pressed reads LOW, exactly as in lesson 07.

## Slide 12
The obvious way, and why it breaks
Lesson 09 | References, Overloading and a Button Class
12
bool isButtonPressed(uint8_t pin) {
static uint8_t previous = HIGH;
static uint32_t last_change_ms = 0U;
// ... the same as in lesson 07 ...
}
isButtonPressed(PIN_A);
isButtonPressed(PIN_B); // the same previous, the same timer
The two buttons now share one memory
Button A writes previous, button B overwrites it, and each one restarts the other's timer. Hold A and press B: B is never counted.

## Slide 13
static belongs to the function
Lesson 09 | References, Overloading and a Button Class
13
One function
One set of static variables, made once, shared by every single call.
Two buttons
Need two memories: two previous states and two timers.
The fix
Move the memory into an object. One object per button.
This is what objects are for
A class describes what one button needs to remember. Every object gets its own copy.

## Slide 14
The Button class
Lesson 09 | References, Overloading and a Button Class
14
class Button {
public:
Button(uint8_t pin);
void begin(void);
bool wasPressed(void);
private:
uint8_t m_pin;
uint8_t m_previous;
uint32_t m_last_change_ms;
};
The two statics became fields
Every object has its own pair
wasPressed() is true once per press
begin() sets INPUT_PULLUP

## Slide 15
Two objects, two memories
Lesson 09 | References, Overloading and a Button Class
15
Button player1(PIN_A);
Button player2(PIN_B);
void loop(void) {
if (player1.wasPressed()) { /* ... */ }
if (player2.wasPressed()) { /* ... */ }
}
A third button is one more line
The debounce logic is written once, inside the class. Each object runs it on its own pin with its own memory.

## Slide 16
PART 4
The Reaction Game
Two players, two buttons, one LED

## Slide 17
The rules
Lesson 09 | References, Overloading and a Button Class
17
The LED is off. Both players wait with a finger on their button.
After a random pause of 2 to 5 seconds, the LED turns green.
The first one to press wins; the LED shows that player's colour.
Press before green and it is a false start: the other player wins.
The serial monitor shows the reaction time and the score.
You already have every part
Two Button objects, the RgbLed class, millis() for time, and one new function: random(), for the pause nobody can guess.

## Slide 18
Summary
Lesson 09 | References, Overloading and a Button Class
18
A reference is a second name; const & passes without a copy and without a pointer
Overloads share a name and differ in their parameters
static belongs to the function, so it cannot tell two buttons apart
An object carries its own state: one Button per button
Homework
Build the two-player reaction game. Details are in homework/README.md.