## Slide 1
LESSON 07
Pointers, Arrays and Strings
Where things live, and how to point at them
Embedded Software Development in C/C++
ESP32-C3 Super Mini | Session 7 of 25

## Slide 2
Today
Lesson 07 | Pointers, Arrays and Strings
2
Arrays: many values under one name
Addresses and pointers: where a value lives, and how to reach it
Why an array and a pointer are almost the same thing
Strings: text is just an array that ends in zero
Last hour: a button, and why one press counts as five
Goal
By the end of the lesson you can pass an array to a function, get two answers back from one call, and build a line of text safely.

## Slide 3
PART 1
Arrays
A row of boxes with one name

## Slide 4
Many boxes, one name
Lesson 07 | Pointers, Arrays and Strings
4
uint8_t readings[5] = { 10U, 20U, 30U, 40U, 50U };
Serial.println(readings[0]); // 10, the first
Serial.println(readings[4]); // 50, the last
Serial.println(sizeof(readings)); // 5 bytes
Counting starts at 0, so five boxes are numbered 0 to 4
All boxes have the same type
The size is fixed when you write the program

## Slide 5
Walking through an array
Lesson 07 | Pointers, Arrays and Strings
5
static const uint8_t COUNT = 5U;
uint8_t readings[COUNT] = { 10U, 20U, 30U, 40U, 50U };
uint16_t sum = 0U;
for (uint8_t i = 0U; i < COUNT; i++) {
sum = sum + readings[i];
}
No error at the edge
readings[5] compiles and runs. It reads whatever happens to sit next to the array. C does not check, so you have to.

## Slide 6
PART 2
Addresses and Pointers
Every box has a number on the door

## Slide 7
Four things to read aloud
Lesson 07 | Pointers, Arrays and Strings
7
uint8_t value = 42U;
uint8_t *p = &value; // p holds the address of value
*p = 7U; // value is now 7
Expression | Read it as | Gives
value | the value | 42, then 7
&value | the address of value | a number like 0x3FC8...
p | the pointer itself | the same address
*p | what p points at | the value in that box

## Slide 8
Where things live
Lesson 07 | Pointers, Arrays and Strings
8
Kind of variable | Lives in | Exists
Global, or static | RAM, a fixed place | the whole time the board runs
Local | the stack, also RAM | only while its function runs
Text in quotes | flash, a different range | forever, and read only
Print the addresses and look
Your numbers will differ from your neighbour's. What matters is which ones sit close together and which one is in a completely different range.

## Slide 9
Changing someone else's variable
Lesson 07 | Pointers, Arrays and Strings
9
void addOne(uint8_t *target) {
*target = *target + 1U;
}
uint8_t count = 5U;
addOne(&count); // count is now 6
The function gets the address
Through it, it changes the original
Without the pointer it would change a copy
Why bother
return hands back one value. Pointers let a function hand back as many as it needs.

## Slide 10
Two answers from one call
Lesson 07 | Pointers, Arrays and Strings
10
void minMax(const uint8_t *values, uint8_t count,
uint8_t *min_out, uint8_t *max_out);
uint8_t lowest;
uint8_t highest;
minMax(readings, COUNT, &lowest, &highest);
const: the function promises to only read the array
count: the function cannot find out the length by itself
_out: the names say which pointers are for answers

## Slide 11
PART 3
Arrays Meet Pointers
And text turns out to be an array too

## Slide 12
An array name is an address
Lesson 07 | Pointers, Arrays and Strings
12
uint8_t *first = readings; // the same as &readings[0]
void show(const uint8_t *values, uint8_t count) {
Serial.println(sizeof(values)); // 4, not the array size
}
sizeof lies inside a function
A passed array arrives as a pointer. sizeof then measures the pointer, 4 bytes on this chip, not the array. That is why the count travels with it.

## Slide 13
A string is an array of char
Lesson 07 | Pointers, Arrays and Strings
13
char greeting[] = "Hi";
Index | 0 | 1 | 2
Content | 'H' | 'i' | '\0'
Two letters take three bytes
The zero at the end is how every function knows where the text stops
Forget it, and printing runs on into whatever memory follows

## Slide 14
Building text safely
Lesson 07 | Pointers, Arrays and Strings
14
char line[32];
snprintf(line, sizeof(line), "%u x %u = %u", a, b, a * b);
Serial.println(line);
The buffer is an array you declared, with a fixed size
snprintf never writes past that size, and always ends with the zero
Here sizeof works: line is a real array, not a passed pointer
Why not String
Arduino String grows on the heap at run time. On a small board that ends in fragments and a crash hours later. A fixed buffer cannot do that.

## Slide 15
One number, three ways to write it
Lesson 07 | Pointers, Arrays and Strings
15
Format | 255 prints as | Meaning
%u | 255 | decimal
%o | 377 | octal, base 8
%X | FF | hexadecimal, base 16
%4u | _255 | at least 4 wide, padded with spaces
const char *FORMATS[] = { "%4o", "%4u", "%4X" };
An array of pointers to strings: every topic of today in one line

## Slide 16
PART 4
The Button
One press, many clicks

## Slide 17
Wiring the button
Lesson 07 | Pointers, Arrays and Strings
17
Button leg | Connects to
One leg | GPIO 0
The other leg | GND
pinMode(BUTTON_PIN, INPUT_PULLUP);
if (digitalRead(BUTTON_PIN) == LOW) {
// pressed
}
No resistor needed
The chip pulls the pin up to 3V3 inside
Pressing connects it to GND
So pressed reads LOW

## Slide 18
One press, five clicks
Lesson 07 | Pointers, Arrays and Strings
18
Metal contacts do not close cleanly; they bounce for a few milliseconds
The chip is fast enough to see every bounce as a separate press
Holding the button down is not the same as pressing it
Press, not hold
React when the pin changes from HIGH to LOW, not while it stays LOW.
Wait it out
After a change, ignore the pin until the contacts have settled.
Solved together, in class
Both need a value that survives between calls. You know which keyword does that.

## Slide 19
Summary
Lesson 07 | Pointers, Arrays and Strings
19
An array is a row of boxes; counting starts at 0 and nothing checks the end
& gives an address, * reaches through it
A passed array is a pointer, so its length travels separately
A string is a char array ending in zero; build it with snprintf
Homework
Print a 16 x 16 multiplication table. The button switches it between octal, decimal and hexadecimal. Details are in the README.