## Slide 1
LESSON 11
Hardware Timers
Interrupts on a schedule, and the rules that keep them safe
Embedded Software Development in C/C++
ESP32-C3 Super Mini | Arduino-ESP32 core 2.x | 2026-10-05
Notes: First K4 session. Last session on the ESP32-C3 before the switch to the Pico in session 12. Students already used attachInterrupt, IRAM_ATTR and volatile once in K3 - today makes those rules explicit.

## Slide 2
Tonight
Lesson 11 | Hardware Timers and Interrupts
2
1
Why timers
2
Timer in the TRM
3
Core 2.x API
4
ISR rules
5
Measure jitter
6
Lab
Goal for tonight
Your board measures its own timing, and you can show in numbers why a hardware timer beats polling.
Notes: About 25 minutes per block, lab gets the last hour. The lab result is the payoff: they prove the point of the lesson with their own measurement.

## Slide 3
PART 1
Why a hardware timer
Polling has a cost you can measure

## Slide 4
Polling: the tick you check for
Lesson 11 | Hardware Timers and Interrupts
4
static const uint32_t PERIOD_US = 1000U;
static uint32_t s_lastUs = 0U;
void loop() {
const uint32_t now = micros();
if (now - s_lastUs >= PERIOD_US) {
s_lastUs = now;
onTick(); // runs only when
} // loop() gets here
readSensors();
updateDisplay();
}
The K3 pattern: no delay(), check the clock
The tick happens when loop() comes back, not when the time is up
Late by up to one full pass of loop()
Jitter: how much the real interval varies around the target
Notes: Ask first: what happens to the tick if updateDisplay() takes 3 ms? Let them answer before the next slide shows it.

## Slide 5
Polling vs a hardware timer
Lesson 11 | Hardware Timers and Interrupts
5
0
1 ms
2 ms
3 ms
4 ms
5 ms
6 ms
Target: every 1 ms
Hardware timer
Polling in loop()
Blocks under the polled ticks: one pass of loop() each. Polling fires at the end of the pass in which the time came due, and the lateness adds up: 5 ticks in 6 ms where 7 were due. The timer stays on the grid.
Notes: The polled ticks are computed from the same rule as the code on the previous slide (last = now). Point at the second polled tick: it is late, and the next period starts from that late moment, so the error never recovers.

## Slide 6
PART 2
From the TRM to the API
Clock, prescaler, counter, alarm

## Slide 7
Inside a timer group
Lesson 11 | Hardware Timers and Interrupts
7
APB_CLK
80 MHz
Prescaler
divide by 2 .. 65536
Counter
54 bits, up or down
Alarm
counter == alarm ?
Interrupt
your ISR runs
auto-reload: counter back to 0
Find it yourself
ESP32-C3 Technical Reference Manual, chapter Timer Group (TIMG). Two groups, one general-purpose timer each - the Arduino core calls them timer 0 and timer 1.
Notes: Have the TRM open on the projector. Students find: number of timers, counter width (54), prescaler width (16 bit, 2..65536), clock sources (APB_CLK or XTAL_CLK). This is the session 4 skill: one specific answer in a long document.

## Slide 8
The arithmetic
Lesson 11 | Hardware Timers and Interrupts
8
80 MHz
APB clock
/
80
divider
=
1 us
one tick (1 MHz)
x
1000
alarm, in ticks
=
1 ms
period (1 kHz)
period = divider x alarm / 80 MHz
A 54-bit counter at 1 MHz overflows after about 570 years. You will not have to wait for it.
Notes: 2^54 us = 1.8e16 us = about 571 years. Divider 80 is the habit because it makes one tick exactly one microsecond, so alarm values read as microseconds.

## Slide 9
Your turn: divider and alarm
Lesson 11 | Hardware Timers and Interrupts
9
Target rate | Period | Divider | Alarm (ticks)
1 kHz (worked example) | 1 ms | 80 | 1000
10 Hz |  |  | 
1 Hz |  |  | 
40 kHz |  |  | 
Fastest possible tick |  |  | -
Hint
Some rows have more than one right answer. Choose the divider first, then check that the alarm is a whole number.
Notes: Answers. 10 Hz: 100 ms, divider 80, alarm 100000. 1 Hz: 1 s, divider 80, alarm 1000000 (or divider 8000, alarm 10000). 40 kHz: 25 us, divider 80, alarm 25. Fastest tick: divider 2 -> 40 MHz -> 25 ns. Divider 1 is not allowed: the range starts at 2.

## Slide 10
Four calls to a periodic interrupt
Lesson 11 | Hardware Timers and Interrupts
10
static const uint8_t TIMER_NUM = 0U; // timer 0 = TIMG0
static const uint16_t TIMER_DIV = 80U; // 80 MHz / 80 = 1 MHz -> 1 us per tick
static const uint64_t ALARM_TICKS = 1000U; // 1000 ticks x 1 us = 1 ms
static hw_timer_t* s_timer = nullptr;
void setup() {
s_timer = timerBegin(TIMER_NUM, TIMER_DIV, true); // true: count up
timerAttachInterrupt(s_timer, &onTick, false); // false: level interrupt
timerAlarmWrite(s_timer, ALARM_TICKS, true); // true: auto-reload, repeat
timerAlarmEnable(s_timer); // arm: interrupts start now
}
onTick is the interrupt service routine. What may go inside it is Part 3.
Notes: Core 2.x signatures: timerBegin(uint8_t num, uint16_t divider, bool countUp), timerAttachInterrupt(timer, fn, bool edge), timerAlarmWrite(timer, uint64_t alarm, bool autoreload), timerAlarmEnable(timer). Edge interrupts are not supported for timers; passing true only logs a warning and falls back to level, so pass false.

## Slide 11
Same idea, two APIs
Lesson 11 | Hardware Timers and Interrupts
11
Core 2.x - what PlatformIO gives you
t = timerBegin(0, 80, true);
timerAttachInterrupt(t, &onTick, false);
timerAlarmWrite(t, 1000, true);
timerAlarmEnable(t);
Core 3.x - what a web search gives you
t = timerBegin(1000000); // Hz
timerAttachInterrupt(t, &onTick);
timerAlarm(t, 1000, true, 0);
How to tell them apart
timerBegin with one argument, or any call to timerAlarm(): that example is core 3.x and will not compile here. Translate it, do not paste it. Same trap as ledcAttach.
Notes: The literals on this slide are only for the side-by-side comparison. In real code they are named constants, as on the previous slide.

## Slide 12
PART 3
ISR discipline
What may and may not run in an interrupt

## Slide 13
Rules for an ISR
Lesson 11 | Hardware Timers and Interrupts
13
Do
Keep it to a few microseconds
Mark it IRAM_ATTR
Make shared variables volatile
Record a value or set a flag
Leave the real work to loop()
Do not
Serial.print or printf
delay() or long loops
new, malloc, String
analogRead()
Anything that waits for something else
An ISR stops everything else. Every microsecond inside it is a microsecond that loop() and every other interrupt wait.
Notes: Why each don't: Serial waits for the USB buffer and takes locks. delay() needs the scheduler. The heap allocator takes a lock that loop() may already hold. analogRead goes through the ADC driver, which is slow and uses locks. IRAM_ATTR keeps the ISR code in RAM so it can run while the flash is busy.

## Slide 14
Flag pattern: the ISR signals, loop() works
Lesson 11 | Hardware Timers and Interrupts
14
volatile bool g_tickFlag = false;
void IRAM_ATTR onTick() {
g_tickFlag = true; // signal only
}
void loop() {
if (g_tickFlag) {
g_tickFlag = false;
doTheWork(); // Serial OK here
}
}
The ISR only records that it happened
loop() does the work at its own pace, with every function allowed
If loop() is slower than the timer, several ticks fold into one flag. A counter instead of a bool tells you how many.
Notes: Same shape as the button ISR in K3, now driven by time instead of a pin.

## Slide 15
PART 4
Measuring and sharing data
Jitter in numbers, and reading it safely

## Slide 16
Let the chip time itself
Lesson 11 | Hardware Timers and Interrupts
16
volatile uint32_t g_lastUs = 0U;
volatile uint32_t g_minUs = UINT32_MAX;
volatile uint32_t g_maxUs = 0U;
volatile uint32_t g_count = 0U;
void IRAM_ATTR onTick() {
const uint32_t now = micros();
const uint32_t dt = now - g_lastUs;
g_lastUs = now;
if (dt < g_minUs) { g_minUs = dt; }
if (dt > g_maxUs) { g_maxUs = dt; }
g_count++;
}
jitter = max - min
Target: 1000 us between ticks
min and max: how far the real interval strays
Unsigned subtraction survives the micros() wrap (about 71 min)
Question
The first report after reset shows a huge max. Why?
Notes: No oscilloscope tonight: the chip measures itself with micros(). Answer to the question: g_lastUs starts at 0, so the first dt is the time since boot. 2^32 us = 4295 s = about 71.6 minutes.

## Slide 17
The snapshot problem
Lesson 11 | Hardware Timers and Interrupts
17
loop(), once per second:
n = g_count
lo = g_minUs
hi = g_maxUs
g_count = 0
ISR: g_count++, new g_maxUs
Two bugs from one interrupt
The new tick is in hi but not in n, so the numbers describe no real second. Then g_count = 0 wipes the tick out completely.
Notes: 32-bit reads are atomic on this chip, so no single value is torn. The problem is that four values are read at four different moments. Ask: how often does this happen? Rarely - which is exactly why it survives testing.

## Slide 18
Copy and reset inside a critical section
Lesson 11 | Hardware Timers and Interrupts
18
portMUX_TYPE g_mux = portMUX_INITIALIZER_UNLOCKED;
void reportOncePerSecond() {
portENTER_CRITICAL(&g_mux); // ISR has to wait
const uint32_t n = g_count;
const uint32_t lo = g_minUs;
const uint32_t hi = g_maxUs;
g_count = 0U;
g_minUs = UINT32_MAX;
g_maxUs = 0U;
portEXIT_CRITICAL(&g_mux); // ISR may run again
Serial.printf("n=%lu jitter=%lu us\n",
(unsigned long)n, (unsigned long)(hi - lo));
}
Between ENTER and EXIT interrupts are held off
Copy and reset only: keep it as short as an ISR
Print outside, from the copies
In the ISR the pair is portENTER_CRITICAL_ISR / portEXIT_CRITICAL_ISR. Required on dual-core chips, cheap here
Notes: This is the critical-section topic deferred from K3. On the single-core C3 the ISR side is not strictly needed, but the canonical pattern has it on both sides and it costs almost nothing. Serial.printf is outside the critical section on purpose.

## Slide 19
PART 5
Lab
Polling vs timer under load

## Slide 20
Lab: polling vs timer under load
Lesson 11 | Hardware Timers and Interrupts
20
1
Polled tick: micros() check in loop(), 1000 us, its own n / min / max
2
Timer tick: the ISR from tonight, same statistics
3
Print both lines once per second
4
Add load: the potentiometer sets how long each loop() pass takes
5
Turn the pot and watch both lines
void loop() {
pollTick();
const uint32_t loadUs =
(uint32_t)analogRead(POT_PIN);
delayMicroseconds(loadUs);
reportOncePerSecond();
}
Pot on GPIO 4: 0 .. about 3850 us of fake work per pass
// Serial output, once per second
poll: n=.... min=.... max=.... jitter=....
timer: n=.... min=.... max=.... jitter=....
Notes: Two separate sets of statistics: the poll set lives only in loop(), the timer set is shared with the ISR. analogRead max is about 3850 counts with the 3.3k series resistor, so the load is roughly 0 to 3.9 ms. delayMicroseconds busy-waits with interrupts enabled, so the timer keeps firing during the load.

## Slide 21
Predict, then measure
Lesson 11 | Hardware Timers and Interrupts
21
Pot position | Poll n | Poll max, us | Timer n | Timer max, us
Left - no load |  |  |  | 
Middle |  |  |  | 
Right - full load |  |  |  | 
Write your prediction first, then the measured value next to it.
Then explain
1. Why does the poll count drop below 1000 per second?
2. The timer max is not exactly 1000 us either. What else runs on this chip?
3. The poll statistics need no critical section. Why not?
Notes: 1: each polled period is 1000 us plus however late loop() was, because last = now restarts the period from the late moment. 2: other interrupts (USB, the FreeRTOS tick) and interrupt entry latency. 3: the poll statistics are written and read only in loop() - one context, nothing interrupts it to touch them.

## Slide 22
Summary
Lesson 11 | Hardware Timers and Interrupts
22
A hardware timer counts on its own: APB 80 MHz -> prescaler -> 54-bit counter -> alarm -> interrupt
period = divider x alarm / 80 MHz; divider 80 gives a 1 us tick
Core 2.x: timerBegin, timerAttachInterrupt, timerAlarmWrite, timerAlarmEnable
ISR: short, IRAM_ATTR, volatile. Record or flag; loop() does the work
Several shared values: copy and reset in a critical section, print outside
Homework
Install the Raspberry Pi Pico platform in PlatformIO before next session - steps in homework/README.md. Next session we move to the Pico. The task is in homework/README.md.
Notes: Remind them: next session starts with soldering headers on the Pico, so the platform must already be installed at home - the download is large.