## Slide 1
LESSON 13
I2C and the AHT10
Two wires, many devices, and a sensor that takes commands
Embedded Software Development in C/C++
Raspberry Pi Pico | Arduino-Pico | Session 13 of 25
Notes: Session 13 of 25, K4. 180 min with two 10-minute breaks. Timeline: 0:00 homework check (20) - 0:20 pull-ups (25) - break - 0:55 protocol on paper (30) - 1:25 wiring and scanner (15) - break - 1:50 lab by hand (50) - 2:40 library (15) - 2:55 summary (5). Hardware: one AHT10 module per pair, instructor keeps the third.

## Slide 2
Today
Lesson 13 | I2C and the AHT10
2
Why I2C lines are open-drain, and why the bus needs pull-ups
Write out an I2C transaction byte by byte: start, address, ACK, data, stop
Register-based vs command-based devices - the AHT10 is the second kind
Find a device with an I2C scanner, and know what to check when it finds nothing
Read the AHT10 by hand with Wire, waiting without delay()
Use a library for the same job - and measure what it costs
Notes: One minute. Point out that the last item comes back as homework.

## Slide 3
Homework Recap: Why It Froze
Lesson 13 | I2C and the AHT10
3
Serial2.print("POT?\n");
// wait for the answer
while (!replyComplete()) {
// the pot side never runs:
// it lives in this same loop()
}
Blocking wait: deadlock
switch (state) {
case State::IDLE:
Serial2.print("POT?\n");
sentAt = millis();
state = State::WAITING;
break;
case State::WAITING:
if (replyComplete()) { /* use it */ }
break;
}
State machine: loop() keeps turning
Keep this pattern in mind
The AHT10 needs about 80 ms per measurement. Today we wait for it the same way.
Notes: 0:00 - 20 min. Ask first: who got it running, who saw it freeze? Let a student explain why: the answering side runs in the same loop(), so while loop() is stuck in the while, nobody answers. replyComplete() is shorthand for the line assembly they already wrote. The fix is the same IDLE / WAITING machine as in the session 12 lab.

## Slide 4
PART 1
Pull-ups
Why a two-wire bus needs two resistors
Notes: 0:20 - start of the electrical block, 25 min including the measurement.

## Slide 5
Push-Pull vs Open-Drain
Lesson 13 | I2C and the AHT10
5
Push-pull
Drives HIGH and drives LOW. This is what digitalWrite() does.
Two outputs on one wire, one HIGH and one LOW: a short circuit.
Open-drain
Can only pull LOW, or let go.
Any number of devices can share one wire. Nobody can fight.
Let go = ?
Nobody drives the line: it floats.
A pull-up resistor makes "let go" mean HIGH.
You have seen this before
INPUT_PULLUP on the K3 buttons: the button pulls LOW, the internal pull-up makes released = HIGH.
Notes: Ask before showing card 3: if every device can only pull low or let go, what is the line when everybody lets go? Answer: undefined, it floats. Value trade-off if asked: smaller resistor = faster rising edges but more current while low. 4.7k is the usual start at 100 kHz.

## Slide 6
One Resistor per Line - Check Your Module
Lesson 13 | I2C and the AHT10
6
3V3
4.7k
SDA
Pico
pull LOW or let go
AHT10
pull LOW or let go
Same again for SCL
Module unpowered, multimeter on ohms
Measure SDA -> VIN and SCL -> VIN
About 4.7k or 10k: pull-ups are on the module
Open circuit: add 4.7k from each line to 3V3
Small 3-pin part near the header? Maybe a regulator: pull-ups may go to its output
3V3 OUT only - never VBUS
Pull-ups to VIN and 5 V on VIN put 5 V on GP4 / GP5. RP2040 pins are not 5 V tolerant.
Notes: Hands-on, pairs, about 10 min. Collect the measured values on the board, one line per module. Before class the instructor has measured all three (Open decision 7) - use that to check the students' numbers, do not hand them the answer. If a module has no pull-ups: hand out 4.7k resistors, two per module.

## Slide 7
PART 2
The Protocol
Start, address, ACK, data, stop
Notes: 0:55 - after the first break. 30 min including the paper exercise.

## Slide 8
One Bus, Many Devices
Lesson 13 | I2C and the AHT10
8
SDA
SCL
Pico
master
AHT10
0x38
another device
its own address
and more:
the same two wires
SCL
SDA
START
STOP
bit 1
bit 0
bit 0
Data changes only while SCL is LOW. SDA changing while SCL is HIGH means START or STOP.
Notes: Two wires shared by everyone, each device has a 7-bit address. The master (the Pico) drives the clock and starts every transaction. Walk through the waveform left to right: idle both high; SDA falls while SCL is high = START; then data bits, each one sampled while SCL is high; SDA rises while SCL is high = STOP. Ask: why can a START never be mistaken for data? Because data never changes while SCL is high.

## Slide 9
The First Byte: Address + R/W
Lesson 13 | I2C and the AHT10
9
A6
A5
A4
A3
A2
A1
A0
R/W
Write
0
1
1
1
0
0
0
0
= 0x70
Read
0
1
1
1
0
0
0
1
= 0x71
address 0x38 = 0111000
Wire takes the 7-bit address (0x38) and adds the R/W bit for you
Some datasheets and forum posts write 0x70 / 0x71 - same device, 8-bit notation
Notes: Do the shift on the board: 0x38 << 1 = 0x70, OR 1 for read = 0x71. The 0x70 notation is a classic source of 'my sensor is not found': someone passes 0x70 to Wire, which shifts it again.

## Slide 10
The 9th Clock: ACK and NACK
Lesson 13 | I2C and the AHT10
10
ACK
After every byte, the receiver pulls SDA LOW for one clock.
"Got it, go on."
NACK on the address
Nobody pulled SDA low: the pull-up wins, the line stays HIGH.
No device at that address - or a loose wire.
NACK at the end
Reading: the master takes the last byte and does not ACK it.
"That is enough, stop sending."
A missing device and a cut wire look the same
Both give NACK. That is why the scanner is the first test, and why the analyzer comes in session 15.
Notes: Link back to the pull-ups: NACK is simply the absence of a pull. Without a pull-up, even that answer is undefined.

## Slide 11
Two Kinds of Devices
Lesson 13 | I2C and the AHT10
11
Register-based (most sensors)
S addr+W A reg A
Sr addr+R A data A data N P
Write a register pointer, then read from it
Sr = repeated start: turn around without releasing the bus
Command-based (the AHT10)
S addr+W A cmd A arg A arg A P
... wait ...
S addr+R A b0 A ... b5 N P
Write a command, wait, read the raw result
No register pointer, no repeated start
Notation for today
S start Sr repeated start P stop A ack N nack addr+W / addr+R = the first byte
Notes: Register-based is theory today: the OPT4001 we planned for is gone, and the AHT10 does not use registers. They will meet register devices in final projects and in the analyzer session. Ask: why is the repeated start needed? So no other master can grab the bus between setting the pointer and reading.

## Slide 12
On Paper: Write Out What Goes Over the Wire
Lesson 13 | I2C and the AHT10
12
1. Start a measurement
Device 0x38.
Command bytes: 0xAC 0x33 0x00.
Write every byte, every A or N, start and stop.
2. Read the result
Device 0x38.
The sensor sends 6 bytes.
Who ACKs each byte? What happens after the last one?
Pairs, 8 minutes
Use the notation from the previous slide. First byte in hex, not as addr+W.
Notes: ANSWER (show on the board after 8 min): Write: S | 0x70 A | 0xAC A | 0x33 A | 0x00 A | P Read: S | 0x71 A | status A | b1 A | b2 A | b3 A | b4 A | b5 N | P In the write, the sensor ACKs every byte. In the read, the master ACKs bytes 0..4 and NACKs byte 5, then stops. Common mistakes: 0x38 instead of 0x70 as the first byte; ACK after the last read byte.

## Slide 13
The Wire API in Six Calls
Lesson 13 | I2C and the AHT10
13
Wire.begin(); // GP4 SDA, GP5 SCL
Wire.beginTransmission(0x38); // start a write
Wire.write(0xAC); // queue bytes
uint8_t err = Wire.endTransmission();
// send; 0 = all ACKed
uint8_t got = Wire.requestFrom(0x38, 6);
// read 6 bytes
uint8_t b0 = Wire.read(); // one byte at a time
Nothing goes on the wire until endTransmission()
err != 0 means a NACK or a bus error
requestFrom() returns how many bytes arrived. Check that too
Always the 7-bit address
Notes: Map each call to the paper exercise: beginTransmission + write + endTransmission = the whole write line; requestFrom = the whole read line including the final NACK and stop. In student code the address and command bytes become named constants at the top of the file - the slide keeps literals for readability.

## Slide 14
Wiring and the I2C Scanner
Lesson 13 | I2C and the AHT10
14
AHT10 | Pico
VIN | 3V3 OUT (pin 36)
GND | GND
SDA | GP4 (pin 6)
SCL | GP5 (pin 7)
for (uint8_t a = 1U; a < 127U; a++) {
Wire.beginTransmission(a);
if (Wire.endTransmission() == 0U) {
Serial.printf("found 0x%02X\n", a);
}
}
Address only, no data: who answers with ACK?
Expected: found 0x38
Empty scan? Check, in this order: 3.3 V at VIN, shared GND, SDA / SCL swapped, pull-ups, pins in code.
Notes: 1:25 - 15 min, pairs. The scanner is in the demo project; they run it as is. Before showing the checklist in the callout, ask the class to build it themselves: what could make the scan come back empty?

## Slide 15
AHT10: A Sensor That Takes Commands
Lesson 13 | I2C and the AHT10
15
Command | Bytes | Then
Init / calibrate | 0xE1 0x08 0x00 | status bit 3 = calibrated
Trigger measurement | 0xAC 0x33 0x00 | wait about 80 ms
Soft reset | 0xBA | wait 20 ms
IDLE
send 0xAC
MEASURING
80 ms passed,
busy bit clear
READ
then back to IDLE - one measurement per second, no delay()
AHT10 is not AHT20
Most examples online are AHT2x code: init 0xBE and a 7th CRC byte. Translate them, do not paste them.
Notes: Same trap family as Arduino-ESP32 core 3.x vs 2.x. If a module never reports calibrated after 0xE1: soft reset 0xBA, try again; if still not set, it may be an AHT20 sold as AHT10 - try 0xBE. The state machine is the session 12 IDLE / WAITING pattern with one more state.

## Slide 16
The 6-Byte Result
Lesson 13 | I2C and the AHT10
16
byte 0
byte 1
byte 2
byte 4
byte 5
hi
lo
byte 3
status
humidity: 20 bits
temperature: 20 bits
Status: bit 7 = busy, bit 3 = calibrated
Raw values go into uint32_t - build them with shifts and masks
RH = raw / 2^20 * 100
T = raw / 2^20 * 200 - 50
2^20 = 1048576
Writing the shifts and masks is the lab
Check your result: breathe on the sensor - humidity jumps within seconds.
Notes: Do not give the unpacking code: it is stage 3 of the lab. For the instructor: hum = (b1 << 12) | (b2 << 4) | (b3 >> 4); temp = ((b3 & 0x0F) << 16) | (b4 << 8) | b5. Cast to uint32_t before shifting. Sanity values: room air 30..60 %RH, 20..25 C.

## Slide 17
Lab: The AHT10 by Hand
Lesson 13 | I2C and the AHT10
17
1. Init
Send the init command, read the status byte.
Print it in hex and as bits. Is bit 3 set?
2. Measure
Trigger, wait 80 ms in a state machine, read 6 bytes.
Print the raw bytes in hex, once per second.
3. Convert
Unpack both 20-bit fields, apply the formulas.
Breathe on it. Hold it between two fingers.
Rules
No delay() in loop(). Named constants for the address and the command bytes. Check every Wire return value.
Notes: 1:50 - 50 min, pairs. Stage 1 about 10 min, stage 2 about 15, stage 3 about 20. Stretch for fast pairs: integer hundredths instead of float (the RP2040 has no FPU). Watch the overflow: raw * 20000 does not fit in 32 bits. If time runs short, stage 3 finishes as part of the homework.

## Slide 18
The Library: Same Numbers, Hidden Cost
Lesson 13 | I2C and the AHT10
18
#include <Adafruit_AHTX0.h>
Adafruit_AHTX0 aht; // aht.begin() in setup()
sensors_event_t hum, temp;
uint32_t t0 = micros();
aht.getEvent(&hum, &temp);
uint32_t dt = micros() - t0;
platformio.ini: lib_deps = adafruit/Adafruit AHTX0
Uses 0xE1, so it works with the AHT10
Inside getEvent(): while busy -> delay(10). No timeout
Measure dt. How long is loop() frozen?
Fine for a logger. Not next to a blink, a UART protocol or a display.
Homework: wrap your by-hand code in a class that never blocks.
Notes: 2:40 - 15 min. Open the library source together (Adafruit_AHTX0.cpp) and find the busy loop - reading other people's drivers is part of the job. Expected dt: about 80 ms. Same micros() method as session 11. Compare the numbers with the by-hand version: they should agree within rounding.

## Slide 19
Summary
Lesson 13 | I2C and the AHT10
19
Open-drain lines + pull-ups: anyone may pull low, nobody can fight
First byte = 7-bit address + R/W; ACK is a pull, NACK is its absence
Register devices use a pointer; the AHT10 takes commands
Scanner first, then the driver; wait in a state machine, not in delay()
Libraries are convenient - measure what they hide
Homework
Class Aht10 with a non-blocking start() / poll(). A reading every 2 s. Sensor unplugged -> "sensor missing" once, and it recovers by itself. Details in homework/README.md.
Notes: 2:55 - 5 min. Modules go home with the students who do the homework. Next session: SPI and the Nokia 5110; the AHT10 reading goes on the display.