## Slide 1
LESSON 14
SPI and the Nokia 5110
Four wires, no ACK, and a display you drive byte by byte
Embedded Software Development in C/C++
Raspberry Pi Pico (RP2040) | PCD8544 | RAII
Notes: Session 14 of 25, K4. Last bus of the three: UART (12), I2C (13), SPI today. Everyone needs: Pico, AHT10 from last time, Nokia 5110, breadboard, wires.

## Slide 2
Today
Lesson 14 | SPI and the Nokia 5110
2
Say how SPI differs from I2C: push-pull, chip select, full duplex, no ACK
Read a clock mode off a timing diagram: the PCD8544 is mode 0
Understand the display memory: 6 banks of 84 bytes, one byte = 8 pixels
Bring the display up from reset with commands and data
Wrap chip select in a RAII class: the K3 idea on real hardware
Show the AHT10 reading on your own display, without delay()
Every lab stage is individual today
Everyone has their own Pico, AHT10 and Nokia 5110. Work next to a partner, help each other, build your own.
Notes: 1 min. Point out the last line: no sharing hardware today.

## Slide 3
Homework Check: the Aht10 Class
Lesson 14 | SPI and the Nokia 5110
3
Show it running: a new reading every 2 s on Serial
Unplug the sensor: "sensor missing" once, then quiet
Plug it back in: readings come back by themselves
Where does loop() wait for the 75 ms conversion?
Keep the class open
Your Aht10 class goes onto the display in lab 3. Today's driver gets the same non-blocking treatment.
Notes: 0:00 - 15 min. Answer to the question: nowhere. loop() starts the measurement, returns, and checks millis() on later passes - the IDLE / WAITING pattern from session 12. If someone blocks for 75 ms: it works, but nothing else in loop() runs meanwhile.

## Slide 4
PART 1
SPI on Paper
Four wires and a clock that the master owns
Notes: 0:15 - 20 min for part 1.

## Slide 5
SPI Next to I2C
Lesson 14 | SPI and the Nokia 5110
5
 | I2C (session 13) | SPI (today)
Wires | SDA, SCL | SCK, MOSI, MISO, CS
Outputs | open-drain + pull-ups | push-pull, no pull-ups
Who listens | 7-bit address in the first byte | the device whose CS is low
Speed | 100 / 400 kHz | MHz (PCD8544: up to 4 MHz)
Direction | one way at a time | both ways on every clock
Acknowledge | ACK / NACK after every byte | none
Another device | same two wires | one more CS wire
Datasheets rename the wires: SCLK, SDI / SDO, SS, CE, SCE. Same signals.
Notes: Contrast every row with last session. Push-pull is why SPI is fast: nobody waits for a pull-up resistor to drag the line high. The last row is the price: no addresses, so every device costs a GPIO.

## Slide 6
Four Wires, One CS per Device
Lesson 14 | SPI and the Nokia 5110
6
Pico
(master)
Nokia 5110
write-only
Another SPI device
(SD card, flash, ...)
SCK ->
MOSI ->
<- MISO
no MISO pin
CS1 -> (GP17)
CS2 ->
SCK, MOSI and MISO are shared. CS is per device: LOW = "you, listen". All other devices ignore the clock.
Notes: Draw attention to CS: active low, one wire per device. A device with CS high must leave MISO alone (it goes high-impedance). The 5110 has no MISO at all: the Pico can talk to it but never hear back. GP16 stays free. D/C and RST are 5110-specific extras, not part of SPI - they come in part 2.

## Slide 7
One Command Byte on the Wire
Lesson 14 | SPI and the Nokia 5110
7
CS
SCK
MOSI
D/C
0
0
1
0
0
0
0
1
LOW = command
bit 7 (MSB)
bit 0
0x21 = 0010 0001: function set, extended instructions
The PCD8544 samples MOSI on every rising SCK edge (dashed lines). D/C is read on the 8th edge.
Notes: Walk the bits left to right. The master changes MOSI while SCK is low and the display reads it on the rising edge - that is mode 0. 8 clocks = 1 byte. At 4 MHz one byte takes 2 us; the whole 504-byte screen about 1 ms.

## Slide 8
Clock Modes: CPOL and CPHA
Lesson 14 | SPI and the Nokia 5110
8
Mode | CPOL | CPHA | SCK idle | Sampled on
0 | 0 | 0 | low | rising edge
1 | 0 | 1 | low | falling edge
2 | 1 | 0 | high | falling edge
3 | 1 | 1 | high | rising edge
CPOL: the level SCK rests at
CPHA: first or second edge samples
The device decides. The datasheet timing diagram says which
PCD8544: mode 0, MSB first, max 4 MHz
const SPISettings LCD_SPI(4000000U, MSBFIRST, SPI_MODE0);
SPI.beginTransaction(LCD_SPI); // speed, order, mode
SPI.transfer(byte); // 8 clocks
SPI.endTransaction();
Notes: Wrong mode does not fail loudly: the device reads every bit half a clock off and you get garbage, or nothing. Session 15 breaks a bus on purpose with a wrong mode. Question: what if we run 8 MHz? Above the rated 4 MHz - may work on one module, fail on the next.

## Slide 9
No ACK, No Scanner
Lesson 14 | SPI and the Nokia 5110
9
I2C
Every byte gets an ACK or a NACK. A missing device is a NACK on the address. The scanner from session 13 lists who answers.
SPI
The master clocks bytes out whether anyone listens or not. A loose wire, a dead display, the wrong mode: no error at all.
So what?
If the screen stays blank, the firmware cannot tell you why. You check wiring, reset, contrast - or you look at the wires.
Session 15
The logic analyzer shows what actually travels on SCK, MOSI, CS and D/C. Install PulseView at home this week.
Notes: This is the motivation for next session. Today, a blank screen means a checklist: power, RST, CE, DC, then contrast. That checklist is on the lab slide.

## Slide 10
PART 2
The PCD8544
The controller inside the Nokia 5110, read from its datasheet
Notes: 0:35 - 20 min for part 2. Have the PCD8544 datasheet open on the projector.

## Slide 11
84 x 48 Pixels in 504 Bytes
Lesson 14 | SPI and the Nokia 5110
11
bank 0
bank 1
bank 2
bank 3
bank 4
bank 5
x = 0
x = 83
one byte: x = 10, bank 1
the byte 0x1F
bit 0 = 1
bit 1 = 1
bit 2 = 1
bit 3 = 1
bit 4 = 1
bit 5 = 0
bit 6 = 0
bit 7 = 0
6 banks x 84 columns = 504 bytes. Bit 0 is the top pixel
After each data byte X moves right; after x = 83 it wraps to the next bank
Notes: The key picture of the session. Pixels are not stored row by row: one byte is a vertical strip of 8 pixels. Ask: how many bytes to clear the screen? 504. How to light the single pixel x = 10, y = 9? Bank 1 (9 / 8), bit 1 (9 % 8), byte 0x02 - but you overwrite the other 7 pixels of that strip. That problem is why libraries keep a framebuffer (part 4).

## Slide 12
The Commands You Need (D/C = 0)
Lesson 14 | SPI and the Nokia 5110
12
Command | Byte | Set | Meaning
Function set | 0x20 / 0x21 | both | H = 0 basic / H = 1 extended
Display control | 0x08 0x0C 0x09 0x0D | basic | blank, normal, all on, inverse
Set Y (bank) | 0x40 ¦ bank | basic | bank 0..5
Set X (column) | 0x80 ¦ x | basic | column 0..83
Temperature coefficient | 0x04 .. 0x07 | extended | TC 0..3
Bias system | 0x10 .. 0x17 | extended | n = 0..7
Set Vop (contrast) | 0x80 ¦ vop | extended | vop 0..127
Same byte, two meanings
0x80 | n is Set X in the basic set and Set Vop in the extended set. Always know which set you are in.
Notes: Show where these come from: the instruction table in the PCD8544 datasheet. Data bytes (D/C = 1) go straight into display RAM at the current X / Y.

## Slide 13
Bringing It Up
Lesson 14 | SPI and the Nokia 5110
13
constexpr uint8_t CMD_FUNC_EXT = 0x21U; // H = 1
constexpr uint8_t CMD_SET_VOP = 0x80U; // | vop
constexpr uint8_t CMD_TEMP_0 = 0x04U;
constexpr uint8_t CMD_BIAS_4 = 0x14U;
constexpr uint8_t CMD_FUNC_BAS = 0x20U; // H = 0
constexpr uint8_t CMD_DISP_NORM = 0x0CU;
constexpr uint8_t VOP_START = 0x31U; // tune
writeCommand(CMD_FUNC_EXT);
writeCommand(CMD_SET_VOP | VOP_START);
writeCommand(CMD_TEMP_0);
writeCommand(CMD_BIAS_4);
writeCommand(CMD_FUNC_BAS);
writeCommand(CMD_DISP_NORM);
First a reset pulse: RST low for a few us, then high
Without it the chip state after power-up is undefined
Vop is the contrast. Every module wants a different value
Blank at every Vop: check RST and CE. Dark blocks: lower Vop
Notes: The reset pulse: digitalWrite(RST, LOW), delayMicroseconds(10U), HIGH. delayMicroseconds in setup() is fine - the no-delay rule is about loop(). Vop 0x31 = 49 is a starting point; clones range roughly 0x28 .. 0x48. Bias 0x13 is the datasheet value for a 1:48 display; 0x14 is what most hobby code uses. If a module looks wrong at every Vop, try the other bias.

## Slide 14
Wiring the 5110 to the Pico
Lesson 14 | SPI and the Nokia 5110
14
Module pin | Signal | Pico GPIO | Pico pin
RST | reset, active low | GP21 | 27
CE (SCE, CS) | chip select, active low | GP17 | 22
DC | LOW = command, HIGH = data | GP20 | 26
DIN | MOSI | GP19 | 25
CLK | SCK | GP18 | 24
VCC | 3.3 V | 3V3 OUT | 36
BL / LIGHT | backlight | see whiteboard | -
GND | ground | GND | any, e.g. 23
3V3 OUT, never VBUS
Wire with USB unplugged. Module labels and pin order differ between boards: go by the label, not the position.
Notes: Same pin map since session 12: SPI0 on the Arduino-Pico default pins, so SPI.begin() needs no pin setup. AHT10 stays on GP4 / GP5 - both fit at once. Backlight: tell them what you found when checking the modules (to GND or to 3.3 V, resistor or not).

## Slide 15
PART 3
RAII: ChipSelect
The constructor takes the bus, the destructor gives it back
Notes: 1:05 - 15 min. This was deferred from K3 on purpose: here it solves a real problem.

## Slide 16
The Early-Return Trap
Lesson 14 | SPI and the Nokia 5110
16
void writeData(const uint8_t* b, size_t n) {
digitalWrite(PIN_CS, LOW);
if (b == nullptr) {
return; // CS stays LOW
}
digitalWrite(PIN_DC, HIGH);
for (size_t i = 0U; i < n; i++) {
SPI.transfer(b[i]);
}
digitalWrite(PIN_CS, HIGH);
}
By hand: every exit must remember CS
void writeData(const uint8_t* b, size_t n) {
ChipSelect cs(PIN_CS);
if (b == nullptr) {
return; // CS released
}
digitalWrite(PIN_DC, HIGH);
for (size_t i = 0U; i < n; i++) {
SPI.transfer(b[i]);
}
} // CS released
With a guard: the destructor runs on every exit
CS stuck LOW gives no error
The next transaction starts in the middle of a byte. The screen shows garbage much later, far from the bug.
Notes: Ask before showing the right side: what goes wrong on the left? Then: how many exits does a real driver function have after a year of changes? The guard ties CS to a scope. Leaving the scope - by return, by falling off the end - releases it.

## Slide 17
The ChipSelect Guard
Lesson 14 | SPI and the Nokia 5110
17
class ChipSelect {
const uint8_t pin_;
public:
explicit ChipSelect(uint8_t pin) : pin_(pin) {
SPI.beginTransaction(LCD_SPI);
digitalWrite(pin_, LOW);
}
~ChipSelect() {
digitalWrite(pin_, HIGH);
SPI.endTransaction();
}
ChipSelect(const ChipSelect&) = delete;
ChipSelect& operator=(const ChipSelect&) = delete;
};
Constructor: take the bus, select the chip
Destructor: release in reverse order
Copying deleted: two guards for one CS would release it twice
Cost after inlining: the same two digitalWrite calls. No heap, no virtual
Notes: Reverse order matters: CS high first, then end the transaction, so another library on the same bus never sees our chip selected. Discussion: what does the guard NOT protect against? Forgetting to create it. Holding it across a long wait - other devices on the bus are locked out meanwhile.

## Slide 18
PART 4
Lab: Your Own Driver
Checkerboard, then text, then the AHT10 on screen
Notes: 1:20. Three stages, all individual. Break between stage 1 and stage 2.

## Slide 19
Lab 1: Reset, Init, Checkerboard
Lesson 14 | SPI and the Nokia 5110
19
USB unplugged: wire the display as on the wiring slide
pinMode for CS, DC, RST; CS starts HIGH; SPI.begin()
writeCommand(uint8_t) and writeData(uint8_t), each with a ChipSelect
Reset pulse, then the init sequence
Clear the screen: 504 data bytes of 0x00
Fill it with 0xAA, 0x55, 0xAA, ... and sweep Vop until it is crisp
Checkpoint before the break
Blank screen checklist
3V3 and GND -> RST pulse in setup() -> CE on GP17 -> DC on GP20 -> sweep Vop. Write your Vop value down.
Notes: 1:20 - 25 min. Goal: a checkerboard on every desk before the break. Why does 0xAA, 0x55 make a checkerboard? 0xAA = 10101010: alternate pixels in the strip; the next column is shifted by one. Common bugs: forgot pinMode on CS, so it floats; DC never set HIGH for data; Vop far too high.

## Slide 20
Lab 2: Text from a Font Table
Lesson 14 | SPI and the Nokia 5110
20
'A' in lab/font5x7.h
7E
11
11
11
7E
-
bit 0
bit 7
column bytes, hex
Characters 0x20 .. 0x7E, 5 bytes each: row n is character 0x20 + n
Same layout as the display RAM: one byte per column, bit 0 on top
5 columns + 1 blank = 6 pixels: 14 characters x 6 lines
gotoXY(col, line), drawChar(char), drawString(const char*)
Outside 0x20 .. 0x7E: draw '?', never read past the table
Stretch: inverse text by sending ~byte
Notes: 1:55 - 30 min. The font is supplied: it is data, not the point of the lab. Students copy lab/font5x7.h into their own src folder. gotoXY: Set X = col * 6, Set Y = line. If text comes out mirrored or upside down, they are reading the table rows instead of the columns, or bit 7 is treated as the top.

## Slide 21
Lab 3: The AHT10 on Your Display
Lesson 14 | SPI and the Nokia 5110
21
One sketch: your Aht10 class and your display code
A new reading every 2 s: millis(), no delay()
Format each line into char line[15]: 14 characters and the terminator
Redraw a line only when its text changed
Breathe on the sensor and watch both numbers move
AHT10 -> 5110
T 23.4 C
RH 41.7 %
ok up 12 min
14 x 6 characters
Tip: fixed point
Keep tenths in an int32_t (234 = 23.4 C) and print the two parts with %ld. No float formatting needed.
Notes: 2:25 - 20 min. snprintf is bounded: it never writes past the 15 bytes. Negative temperatures with the fixed-point tip: watch the sign of the tenths part (-0.5 C). A good homework question. Redraw only changed lines: compare with the previous text, keep the old buffer.

## Slide 22
The Same Screen through a Library
Lesson 14 | SPI and the Nokia 5110
22
Adafruit_PCD8544 lcd(PIN_DC, PIN_CS, PIN_RST);
lcd.begin();
lcd.setContrast(LCD_CONTRAST);
lcd.clearDisplay(); // RAM buffer only
lcd.setCursor(0, 16);
lcd.print("T ");
lcd.print(temp.temperature, 1);
lcd.display(); // now it is sent
demo/src/main.cpp, shortened
A 504-byte framebuffer in RAM: draw into it, then display()
display() sends the changed rectangle; after clearDisplay() that is all 504 bytes
CS, D/C and SPI settings handled inside
Init sequence behind begin(): bias, Vop, no temperature coefficient
Three libraries: PCD8544, GFX, BusIO
Is 504 bytes of RAM a problem?
Not on the RP2040 (264 KB). On an ATmega328 (2 KB) it was a quarter of all RAM.
Notes: 2:45 - 10 min. Run the demo. The framebuffer solves the problem from the memory map slide: setPixel can change one bit and keep the other seven. begin() first shows the Adafruit splash image that lives in the buffer at start-up; the demo clears it.

## Slide 23
Summary
Lesson 14 | SPI and the Nokia 5110
23
SPI: push-pull, one CS per device, full duplex, no ACK - and so no errors
The device picks the clock mode; the PCD8544 is mode 0, up to 4 MHz
PCD8544 RAM: 6 banks x 84 bytes, one byte = 8 vertical pixels
ChipSelect: CS follows the scope, on every exit
A library buys a framebuffer and fonts for 504 bytes of RAM
Homework
Dashboard on your own driver: T, RH, min / max, SENSOR MISSING and recovery. Install PulseView and check your analyzer. Details: homework/README.md.
Notes: 2:55 - 5 min. Next session: the logic analyzer. Your UART, I2C and SPI code from sessions 12-14 is what we capture, so keep it working.