## Slide 1
LESSON 17 | OPTIONAL BLOCK S1
STM32: Working Demo
Ready CubeMX project, DFU upload, two I2C sensors
Embedded Software Development in C/C++
Session 17 | 4 academic hours
Notes: Plan (4 x 45 min): pull and build 20 min, DFU upload 20, bare-board output 10, wiring and sensors 30, app.c tour 30, homework start in class the rest. Goal: every pair sees real sensor values within the first hour.

## Slide 2
Today
Lesson 17 | STM32: From Project to Working Demo
2
Last time CubeMX took most of the session - today the project is ready
Pull -> build -> upload over USB (DFU) -> see the output
First on a bare board, then with the GY-521 and the BH1750
A tour of app.c: how our code sits next to the generated code
Start the homework in class: night light and orientation
The project
M4_L17/lesson16 - the full CubeMX project from session 16, tested on a real Black Pill.

## Slide 3
Recap: Session 16 in Four Ideas
Lesson 17 | STM32: From Project to Working Demo
3
CubeMX
Pins, clocks and peripherals are clicked once. CubeMX writes the init code in C.
96 MHz
USB needs exactly 48 MHz. 96 / 2 = 48 works, 100 MHz does not.
HAL
Explicit calls: port and pin, handle, timeout, a return status to check.
app.c
Our code. main.c only calls app_init() and app_loop() in USER CODE.
All four are already done in today's project
Nothing to click in CubeMX today. We use the result and look inside it.

## Slide 4
PART 1
Build and Upload
From git pull to a blinking LED

## Slide 5
Step 1: Open and Build
Lesson 17 | STM32: From Project to Working Demo
5
git pull
Course repository
->
Open Folder
M4_L17/lesson16 - the folder with the .ioc
->
Set Up
STM32Cube panel -> Set Up project -> Debug
->
Build
F7 -> build/Debug/ lesson16.elf
RAM: 12720 B 128 KB 9.70%
FLASH: ~41 KB 512 KB ~8%
Expected at the end of the build
Open the project folder, not the repository root
Otherwise the STM32 extension finds no CMakeLists.txt and offers nothing to build.

## Slide 6
Step 2: Upload over USB (DFU)
Lesson 17 | STM32: From Project to Working Demo
6
Hold BOOT0
and keep holding
->
Tap NRST
press and release
->
Release BOOT0
LED stays dark: ROM bootloader runs
STM32CubeProgrammer | Setting
Connection | USB, refresh, port USB1 -> Connect
File path | build/Debug/lesson16.elf
Start address | empty - the .elf knows it
Verify / Run after programming | both ticked
No USB1? Data cable (not charge-only) and repeat BOOT0 + NRST.

## Slide 7
Red at the End Is Normal
Lesson 17 | STM32: From Project to Working Demo
7
Download verified successfully
RUNNING Program ...
Start operation achieved successfully
Warning: Connection to device 0x431 is lost
Error: Establishing connection with device failed
Last lines of the CubeProgrammer log
Look for: verified successfully
Then the chip leaves the bootloader
The DFU device disappears from USB
CubeProgrammer cannot reconnect: red
Your program is running
The red line means the bootloader is gone - exactly what we want. A new COM port appears instead.

## Slide 8
Step 3: Bare Board First
Lesson 17 | STM32: From Project to Working Demo
8
Lesson 16 - STM32F411 Black Pill, HAL, USB CDC
SYSCLK 96000000 Hz
I2C1 scan (PB6 SCL, PB7 SDA):
0 device(s)
MPU-6050 not found at 0x68
BH1750 not found at 0x23
Press KEY to show this again.
5265 ms lux n/a acc n/a
VS Code Serial Monitor, any baud rate
Clock: correct
USB virtual COM port: works
I2C: nothing on the bus yet
Port opened late? Press KEY
One thing at a time
Clock and USB are proven before a single wire is added. If the sensors fail later, the problem is the wiring.

## Slide 9
Step 4: Wire the Sensors
Lesson 17 | STM32: From Project to Working Demo
9
Module pin | GY-521 (MPU-6050) | BH1750 | Black Pill
VCC | VCC | VCC | 3V3
GND | GND | GND | GND
SCL | SCL | SCL | PB6
SDA | SDA | SDA | PB7
Address | 0x68 (AD0 low) | 0x23 (ADDR low) | -
3V3 only, never 5V
Both modules carry their own pull-up resistors. Two sensors share the same two wires: that is the point of a bus.

## Slide 10
With Sensors: What You Should See
Lesson 17 | STM32: From Project to Working Demo
10
I2C1 scan (PB6 SCL, PB7 SDA):
0x23
0x68
2 device(s)
MPU-6050 WHO_AM_I = 0x68 (0x68 on a genuine part)
BH1750 ok
4512 ms lux 213.3 acc 12 -40 1003 mg temp 26.4 C
Press KEY after wiring: the scan runs again
Scan still empty? | Check
Module LED off | VCC on 3V3, GND on GND
LED on, 0 devices | SCL and SDA swapped? SCL = PB6, SDA = PB7

## Slide 11
PART 2
Inside app.c
Where our code lives and how it runs

## Slide 12
app.c: A Small State Machine
Lesson 17 | STM32: From Project to Working Demo
12
/* main.c, USER CODE 2 */
app_init();
/* main.c, USER CODE 3 */
while (1) {
app_loop();
}
The only lines we add to main.c
WAIT_USB
LED blinks fast
->
GRACE
2 s to open the port
->
RUN
every 500 ms: read, print
app_loop() never blocks: it checks HAL_GetTick() and returns
Cable pulled -> back to WAIT_USB
Generate Code in CubeMX leaves app.c untouched

## Slide 13
Two Sensors, Two Styles
Lesson 17 | STM32: From Project to Working Demo
13
/* MPU-6050: registers */
HAL_I2C_Mem_Read(&hi2c1, MPU_ADDR,
0x3B, I2C_MEMADD_SIZE_8BIT,
b, 14, I2C_TIMEOUT_MS);
/* write 0x3B, repeated START,
read 14 bytes: accel, temp, gyro */
/* BH1750: commands, no registers */
bh_send(0x01); /* power on */
bh_send(0x10); /* continuous H */
HAL_I2C_Master_Receive(&hi2c1,
BH_ADDR, b, 2, I2C_TIMEOUT_MS);
/* lux = raw / 1.2 */
Same bus, different conversation
HAL wants the address shifted left by one: 0x68 << 1. No %f in printf (newlib-nano), so values are printed in tenths.

## Slide 14
Homework 17
Lesson 17 | STM32: From Project to Working Demo
14
Night light
Below 10 lx: LED on. 10..300 lx: toggles. Above 300 lx: off. Limits are named constants.
Orientation
az >= 700 mg: FLAT. az <= -700 mg: UPSIDE DOWN. Otherwise ON EDGE. Printed at the end of each line.
Extra
Print "-> now UPSIDE DOWN" once per change. Hint: a static variable.
Work in your own copy
Copy M4_L17/lesson16 to homework/<name>/lesson16. Change only Core/Src/app.c. Details: homework/README.md.

## Slide 15
Summary
Lesson 17 | STM32: From Project to Working Demo
15
A generated project is a normal folder: open, set up, build
DFU: BOOT0 + NRST, .elf without a start address, red at the end is fine
Bring up in order: clock -> USB -> bus -> sensors
MPU-6050 is register based, BH1750 is command based
Our code stays in app.c, so CubeMX can regenerate at any time
Homework
Night light and orientation in app.c - see M4_L17/homework/README.md.