## Slide 1
LESSON 10
States, Templates and Interrupts
C++ that fits in 400 kB
Embedded Software Development in C/C++
ESP32-C3 Super Mini | Session 10 of 25

## Slide 2
Today
Lesson 10 | States, Templates and Interrupts
2
Your reaction game is a state machine, and enum class gives the states names
Why we stay away from new, String and std::vector on a microcontroller
Templates: one class for any type, with its size fixed before the program runs
Interrupts: letting the hardware tell you a button was pressed
Goal
By the end of the lesson you can store a history of values without the heap, and catch a button press the moment it happens.

## Slide 3
PART 1
State Machines
What your game already was

## Slide 4
Your game, drawn as states
Lesson 10 | States, Templates and Interrupts
4
State | LED | What can happen | Next state
Waiting | off | the pause ends / someone presses early | Go / Result
Go | green | a press | Result
Result | winner's colour | two seconds pass | Waiting
This has a name: a state machine
The program is always in exactly one state. Events move it to the next one. Most firmware you will ever read is built this way.

## Slide 5
Names for the states: enum class
Lesson 10 | States, Templates and Interrupts
5
enum class State : uint8_t {
Waiting,
Go,
Result
};
State g_state = State::Waiting;
Names, not numbers
State::Go cannot be mixed up with 1, or with another enum
: uint8_t keeps it one byte

## Slide 6
loop() asks one question
Lesson 10 | States, Templates and Interrupts
6
void loop(void) {
switch (g_state) {
case State::Waiting: handleWaiting(); break;
case State::Go: handleGo(); break;
case State::Result: handleResult(); break;
}
}
One state, one function
loop() only asks where are we. Each handler decides what happens next and changes g_state when it is time to move on.

## Slide 7
PART 2
Memory Without Surprises
What to avoid, and what to use instead

## Slide 8
What we leave out, and why
Lesson 10 | States, Templates and Interrupts
8
Avoid | Why | Instead
new, delete, malloc | memory carved up while running; it fragments | arrays and objects made once
String | grows on the heap behind your back | char buffers and snprintf
std::vector | the same heap, plus copies when it grows | a fixed-size template: today
exceptions | big code, hidden paths, often switched off | return a status
RTTI, dynamic_cast | flash spent on type information | know your types by design
The failure comes hours later
A board that allocates and frees for a whole night ends up with plenty of free memory in pieces too small to use. It crashes, and nothing points at the cause.

## Slide 9
One function for any type
Lesson 10 | States, Templates and Interrupts
9
template <typename T>
T largest(T a, T b) {
return (a > b) ? a : b;
}
largest(3U, 7U); // T is unsigned
largest(-40, 12); // T is int
T is a placeholder for a type
The compiler fills it in at each call
A template costs flash, not RAM
The compiler writes one copy of the function for every type you actually use, and none for the types you do not.

## Slide 10
A class template: RingBuffer
Lesson 10 | States, Templates and Interrupts
10
template <typename T, uint8_t N>
class RingBuffer {
public:
void push(T value);
uint8_t count(void) const;
T at(uint8_t index) const; // 0 is the oldest
private:
T m_items[N];
uint8_t m_next = 0U;
uint8_t m_count = 0U;
};
T: what is stored
N: how many, fixed when you compile
const after a method: it only reads
sizeof is known; nothing is allocated while running

## Slide 11
Round and round
Lesson 10 | States, Templates and Interrupts
11
void push(T value) {
m_items[m_next] = value;
m_next = (uint8_t)((m_next + 1U) % N); // after the last: 0
if (m_count < N) {
m_count++;
}
}
Full is not a problem
Once all N places are used, the newest value simply overwrites the oldest. The buffer always holds the last N values, in the same memory, forever.

## Slide 12
PART 3
Smoothing the Knob
The averaging from lesson 05, done properly

## Slide 13
A moving average
Lesson 10 | States, Templates and Interrupts
13
RingBuffer<uint16_t, 16> samples;
samples.push((uint16_t)analogRead(POT_PIN));
uint32_t sum = 0U;
for (uint8_t i = 0U; i < samples.count(); i++) {
sum += samples.at(i);
}
const uint16_t smooth = (uint16_t)(sum / samples.count());
One new reading per pass, not sixteen
In lesson 05 we took 16 readings in a row and waited for all of them. Now each pass adds one, and the average always covers the last 16.

## Slide 14
PART 4
Interrupts
Let the hardware call you

## Slide 15
Asking all the time, or being told
Lesson 10 | States, Templates and Interrupts
15
 | Polling | Interrupt
Who checks | loop(), over and over | the hardware, by itself
Reacts | when loop() gets round to it | within microseconds
Can miss | anything shorter than one pass | nothing
Costs | nothing, it is simple | rules you must follow
Why the game wants it
The press is stamped with the time the moment it happens, not when loop() notices. Reaction times become fair to the microsecond.

## Slide 16
attachInterrupt
Lesson 10 | States, Templates and Interrupts
16
static volatile uint32_t g_pressed_at_us = 0U;
static volatile bool g_pressed = false;
void IRAM_ATTR onButtonA(void) {
g_pressed_at_us = micros();
g_pressed = true;
}
attachInterrupt(digitalPinToInterrupt(PIN_A), onButtonA, FALLING);
FALLING: from HIGH to LOW, the moment of the press
loop() checks g_pressed, does the real work, and clears it

## Slide 17
The rules for an interrupt handler
Lesson 10 | States, Templates and Interrupts
17
Keep it short: note what happened, leave the work to loop()
No Serial, no delay(), nothing that waits
Variables shared with loop() are volatile
IRAM_ATTR keeps the handler in RAM, ready at any moment
Bounce does not go away
One press can fire the interrupt five times. The handler sees every bounce, just faster than loop() ever could. Debouncing is still your job.

## Slide 18
Summary
Lesson 10 | States, Templates and Interrupts
18
A state machine: one state at a time, events move it on; enum class names the states
No heap at run time: fixed arrays, char buffers, objects made once
A template is written once and works for any type; N fixes the size in advance
An interrupt reacts at once, and its handler must stay short and simple
Homework
Extend the reaction game with a history of the last 10 reaction times per player in a RingBuffer. Details are in homework/README.md.