## Slide 1
LESSON 04
Soldering
Make the joint, then find the answer
Embedded Software Development in C/C++
Block K2 | Session 4 of 25 | 4 academic hours

## Slide 2
Goals for Today
Lesson 04 | Soldering and Documentation
2
Solder header pins to a board and get joints that hold
Tell a good joint from a cold joint and a bridge
Check your own work with a multimeter
Know which document answers which kind of question
Find one specific number in an 800-page datasheet
Use AI as a search aid without trusting its numbers
This closes block K2
After today we start programming the ESP32-C3 in C.

## Slide 3
Homework Review
Lesson 04 | Soldering and Documentation
3
Problem | Answer
1 - resistor for red LED | 130 ohm
2 - resistor for blue LED | 20 ohm
3 - power in the resistor | 0.013 W (13 mW)
4 - resistance from measurement | 1031 ohm
5 - minimum pull-up value | 6600 ohm (6.6 kohm)
Hold on to problem 5
You calculated a minimum pull-up of 6.6 kohm. Later today the datasheet tells us what the chip actually uses.

## Slide 4
PART 1
Soldering
On Monday you watched. Today you solder.

## Slide 5
What We Are Working With
Lesson 04 | Soldering and Documentation
5
Property | Value
Solder alloy | Sn99 Cu0.7 Ag0.3, lead free
Wire diameter | 0.7 mm
Flux | Rosin core, 3 percent, inside the wire
Melting point | about 227 C
Iron temperature | 350 C
No extra flux needed
The flux is already inside the solder wire. For header pins on a clean board that is enough.

## Slide 6
Lead-Free Behaves Differently
Lesson 04 | Soldering and Documentation
6
Lead-free melts at about 227 C. The old tin-lead alloy melted at 183 C
That is why the iron sits at 350 C and not lower
It flows less eagerly and gives you a smaller window to work in
A finished joint looks matte and slightly grainy, not mirror shiny
Matte is normal, not a cold joint
Most soldering photos online show tin-lead solder, which is shiny. Do not re-melt a good lead-free joint just because it looks dull.

## Slide 7
Making One Joint
Lesson 04 | Soldering and Documentation
7
1. Wipe the tip and tin it. A dry oxidised tip transfers almost no heat
2. Touch the tip to the pin and the pad at the same time
3. Wait about one second, then feed solder into the joint, not onto the tip
4. Let it flow around the pin, then remove the solder, then the iron
5. Total contact time 2 to 3 seconds per pin
If it is not flowing, do not wait longer
Raise the temperature toward 370 C instead. Holding a cool iron on a pad for ten seconds lifts the pad off the board.

## Slide 8
Three Outcomes
Lesson 04 | Soldering and Documentation
8
Good
Solder has wetted both the pin and the pad. Smooth cone shape. Matte surface. Nothing moves when you push the pin.
Cold
A blob sitting on the pad without wetting it. Often cracked or lumpy. Works today, fails in a month when the board is moved.
Bridge
Solder connecting two neighbouring pins. The most common beginner fault and the easiest to find with a multimeter.
A cold joint is worse than an obvious failure
It passes the first test and fails later, somewhere else, for no visible reason.

## Slide 9
Safety
Lesson 04 | Soldering and Documentation
9
The tip is at 350 C. It burns on contact and stays hot long after switch off
The iron lives in its holder. Never on the bench, never hanging over an edge
The smoke is flux, not solder. Do not lean over the joint while it melts
Wash your hands before eating, even with lead-free solder
Solder splashes: no leaning over, and keep your eyes out of the plane of work
If something goes wrong
Burn: cold running water, tell the instructor. Dropped iron: let it fall, do not catch it.

## Slide 10
Your Task
Lesson 04 | Soldering and Documentation
10
A spare ESP32-C3 Super Mini and a set of header pins, one per person
Seat the header in the holes, board flat on the bench
Solder one corner pin first, check the header sits straight, then do the rest
If the header is crooked, reheat that single corner pin and adjust
Work through the row pin by pin. Speed is not the goal today
One corner pin first
Solder the whole row before checking alignment and you get to desolder the whole row.

## Slide 11
Check Your Own Work
Lesson 04 | Soldering and Documentation
11
Multimeter in continuity mode - the same tool you used on Monday
Between each pin and its pad: must beep. No beep means a cold joint
Between neighbouring pins: must stay silent. A beep means a bridge
Then look at every joint against the three outcomes we just covered
This is the debugging habit, not an extra step
You now have a tool that finds the fault before the board is ever powered. Measuring beats assuming - the same rule as Monday.

## Slide 12
PART 2
Reading Documentation
Where the rules we have been using actually come from

## Slide 13
Three Documents, Three Jobs
Lesson 04 | Soldering and Documentation
13
Datasheet
What the chip IS. Pins, voltages, currents, limits, packaging. Go here for a number.
Reference Manual
How the chip WORKS. Registers, peripherals, bit fields. Go here to program something.
Application Note
How to USE it for one task. Worked examples and recommended circuits.
For the ESP32-C3
Datasheet is about 75 pages. The Technical Reference Manual is over 1000. Picking the right one first saves most of the search.

## Slide 14
Finding One Answer in 800 Pages
Lesson 04 | Soldering and Documentation
14
Never read forward from page one. You are looking something up, not reading a book
Start with the table of contents, then the list of tables - numbers live in tables
Search for the unit, not the concept: mA, kohm, V, not 'how much current'
Learn the standard symbols: VIH, VIL, IOH, IOL, RPU. They are the same across vendors
Note the document version. Values and page numbers move between revisions
Our document today
ESP32-C3 Series Datasheet v2.4. Electrical Characteristics is Section 5.

## Slide 15
Worked Example: Pin Drive Current
Lesson 04 | Soldering and Documentation
15
Question from Monday: we said 'tens of milliamps'. Where is the real number?
Contents -> Section 5 Electrical Characteristics -> 5.4 DC Characteristics
Table 5-4 lists IOH, high-level source current: 40 mA typical
But Table 2-1 note 4 gives the DEFAULT drive strength: 20 mA for GPIO 8
Two numbers, both correct. One is the ceiling, one is what you get unconfigured
This is why you read the whole row
The conditions column matters. 40 mA is quoted at PAD_DRIVER = 3, not at the default setting.

## Slide 16
Monday's Rules, Now With Sources
Lesson 04 | Soldering and Documentation
16
We said | Datasheet says | Where
Logic is 3.3 V | VIH min 0.75 x VDD = 2.48 V | Table 5-4
LOW is near 0 V | VIL max 0.25 x VDD = 0.83 V | Table 5-4
Tens of milliamps | 20 mA default, 40 mA max | Table 2-1, 5-4
GPIO 9 has a pull-up | RPU = 45 kohm | Table 5-4
GPIO 8 and 9 are strapping | Boot mode control | Table 3-3
Your homework answer, checked
You calculated a 6.6 kohm minimum pull-up. The chip uses 45 kohm - well above your floor, and chosen to waste less current.

## Slide 17
PART 3
AI as a Documentation Tool
Useful for finding, unreliable for knowing

## Slide 18
Where It Helps, Where It Lies
Lesson 04 | Soldering and Documentation
18
Good At
Explaining an unfamiliar term. Telling you which document and which section to open. Summarising a concept you have no vocabulary for yet.
Bad At
Exact numbers. Pin assignments. Chip variants. It will confidently answer for ESP32 when you asked about ESP32-C3, and they are different chips.
The failure mode is confidence
A wrong answer arrives in the same tone as a right one. There is no uncertainty marker to notice.

## Slide 19
The Working Rule
Lesson 04 | Soldering and Documentation
19
AI -> where to look
Datasheet -> what the answer is
An answer without a section or table number is not an answer yet
If the AI names a table, open that table and read it yourself
If it cannot name one, treat the number as a guess
This is the same standard you would apply to a colleague's memory

## Slide 20
Summary
Lesson 04 | Soldering and Documentation
20
Lead-free solder at 350 C, flux already in the wire, matte joints are fine
Good joint, cold joint, bridge - and how to tell them apart
Continuity check finds your own faults before power is applied
Datasheet for numbers, reference manual for registers
AI points at the section, the datasheet gives the value
Homework
Datasheet lookup: six numbers, each with the table it came from. See homework/README.md