## Slide 1
LESSON 06
Functions, Scope and Bits
Naming your own work, and reading a number bit by bit
Embedded Software Development in C/C++
ESP32-C3 Super Mini | Session 6 of 25

## Slide 2
Today
Lesson 06 | Functions, Scope and Bits
2
Writing your own functions instead of only calling ours
Where a variable is visible, and how long it stays alive
The stack: what happens on every call and every return
Bits, masks and shifts
Last hour: an RGB LED that shows the temperature as a colour
Goal
By the end of the lesson you can write a function, explain why a local variable forgets, and turn a number into a pattern of lights.

## Slide 3
PART 1
Functions
A name for a piece of work

## Slide 4
You have already used functions
Lesson 06 | Functions, Scope and Bits
4
uint16_t counts = readPotentiometer();
int16_t f = mapToFahrenheit(counts);
Someone wrote them, you called them
A name, some input, one answer back
You did not need to know what was inside
Today you write your own

## Slide 5
The four parts of a function
Lesson 06 | Functions, Scope and Bits
5
int16_t doubleIt(int16_t value) {
return value * 2;
}
int16_t - what comes back
doubleIt - the name you call
(int16_t value) - what goes in
return - the answer leaving
One job each
A function that does one thing has a name that says what it does. If the name needs the word and in it, it is two functions.

## Slide 6
The compiler reads top to bottom
Lesson 06 | Functions, Scope and Bits
6
void printBinary(uint8_t value); // prototype
void loop(void) {
printBinary(42U); // call
}
void printBinary(uint8_t value) { // the real thing
// ...
}
Call before the body?
Then announce it first
That line is the prototype

## Slide 7
PART 2
Scope and the Stack
Where a variable lives and when it disappears

## Slide 8
Where a variable is visible
Lesson 06 | Functions, Scope and Bits
8
static uint8_t g_total = 0U; // the whole file
void demo(void) {
uint8_t local = 0U; // this function only
local = local + 1U;
}
The braces are the boundary
Outside them the name does not exist
Two functions can each have a local called value; they are different variables

## Slide 9
What a call actually does
Lesson 06 | Functions, Scope and Bits
9
Call
A frame is put on the stack: the parameters and the locals.
Work
The function uses its own frame and nobody else's.
Return
The frame is dropped. The locals go with it.
The stack is small
A few kilobytes, not megabytes. Large local arrays and deep chains of calls are how a board runs out of it.

## Slide 10
The variable that remembers
Lesson 06 | Functions, Scope and Bits
10
void countCalls(void) {
static uint8_t calls = 0U;
calls = calls + 1U;
Serial.println(calls);
}
Created once, not on every call
Prints 1, 2, 3, 4 ...
Without static: 1, 1, 1, 1
Keep this one in mind
Tonight's star task needs a value that survives from one call to the next.

## Slide 11
PART 3
Bits
Looking inside a byte

## Slide 12
One byte, eight bits
Lesson 06 | Functions, Scope and Bits
12
Value | Bits | Which bits are set
0 | 00000000 | none
1 | 00000001 | bit 0
5 | 00000101 | bit 0 and bit 2
128 | 10000000 | bit 7
255 | 11111111 | all of them
Counting from the right
Bit 0 is worth 1, bit 1 is worth 2, bit 2 is worth 4, and so on up to 128.

## Slide 13
Your first function from scratch
Lesson 06 | Functions, Scope and Bits
13
void printBinary(uint8_t value) {
for (int8_t i = 7; i >= 0; i--) {
Serial.print((value >> i) & 1U);
}
Serial.println();
}
Shift the bit you want down to the bottom
Mask away everything else
Bit 7 first, bit 0 last

## Slide 14
Four operations, that is all
Lesson 06 | Functions, Scope and Bits
14
value & 1U // is bit 0 set?
value | 4U // switch bit 2 on
value >> 2 // move the bits right
value << 2 // move the bits left
& asks a question
| sets something
Shifts move, they do not add
One character apart
& and && are different operators. So are | and ||. The compiler accepts both and only one of them does what you meant.

## Slide 15
PART 4
The Colour Thermometer
Datasheet, wiring, and tonight's homework

## Slide 16
What the LED datasheet says
Lesson 06 | Functions, Scope and Bits
16
Parameter | Red | Green | Blue
Forward voltage, typical | 1.95 V | 3.3 V | 3.3 V
Continuous current, max | 30 mA | 30 mA | 30 mA
Brightness at 20 mA | 1500 mcd | 5000 mcd | 1500 mcd
Measured on the bench
With 100 ohm all three look right. With 200 ohm the red one goes dim first, even though it has the most voltage to spare. The last row explains why.

## Slide 17
Wiring the RGB LED
Lesson 06 | Functions, Scope and Bits
17
LED pin | Connects to | Through
Longest pin, common anode | 3V3 | direct
Red | GPIO 5 | 100 ohm
Green | GPIO 6 | 100 ohm
Blue | GPIO 7 | 100 ohm
Common anode means backwards
LOW switches a colour ON. HIGH switches it OFF. The same logic as the LED on the board itself.

## Slide 18
A colour is three bits
Lesson 06 | Functions, Scope and Bits
18
Blue | Green | Red | Colour | Temperature band
1 | 0 | 0 | blue | cold
1 | 1 | 0 | cyan | cool
0 | 1 | 0 | green | normal
0 | 1 | 1 | yellow | warm
0 | 0 | 1 | red | hot
Three switches, eight colours
Bit 0 is red, bit 1 is green, bit 2 is blue. Five of the eight combinations are used here.

## Slide 19
Summary
Lesson 06 | Functions, Scope and Bits
19
A function has a name, its input, and one result
A local variable dies at the closing brace; static survives the return
Every call pushes a frame on the stack and every return drops it
Bits are read with a shift and a mask
Homework
Build the colour thermometer: the knob sets the temperature, the LED shows the band. Star task: stop the colour flickering at the edge of a band.