## Slide 1
LESSON 03
Electrical Fundamentals
Measure instead of assuming
Embedded Software Development in C/C++
Block K2 | Session 3 of 25 | 4 academic hours

## Slide 2
Goals for Today
Lesson 03 | Electrical Fundamentals
2
Predict what a circuit does before you build it
Use Ohm's law to pick a resistor instead of guessing
Recognise the common passive components and their purpose
Explain why a pull-up makes a pressed button read LOW
State what a GPIO pin can and cannot drive
Measure voltage, current and resistance with a multimeter
No firmware today
Bring the board with the lesson 02 blink still on it. We measure the program you already wrote.

## Slide 3
PART 1
Voltage, Current, Resistance
The three quantities everything else is built from

## Slide 4
Think of Water in a Pipe
Lesson 03 | Electrical Fundamentals
4
Electrical | Water | Unit
Voltage | Pressure in the pipe | volt (V)
Current | Flow rate through it | amp (A)
Resistance | How narrow the pipe is | ohm
Why the analogy helps
Raise the pressure and more water flows. Narrow the pipe and less does. That is Ohm's law before any algebra.

## Slide 5
Ohm's Law
Lesson 03 | Electrical Fundamentals
5
V = I * R
I = V / R how much current will flow
R = V / I what resistor do I need
V = I * R how much voltage is dropped
Three forms of one equation
Current in datasheets is in milliamps
Ohm's law needs amps
10 mA = 0.010 A
Getting this wrong is the most common error

## Slide 6
Power: Where the Heat Goes
Lesson 03 | Electrical Fundamentals
6
P = V * I
P = I * I * R when you know current and resistance
Power matters for LEDs and resistors, where energy becomes heat and light
It matters much less for GPIO logic signals, where currents are tiny
A standard through-hole resistor is rated for 0.25 W
Exceed that rating and the resistor cooks, discolours and drifts

## Slide 7
Why 3.3 V and Not 5 V
Lesson 03 | Electrical Fundamentals
7
Logic is 3.3 V
The ESP32-C3 runs its logic at 3.3 V. A GPIO input expects at most that.
5 V Damages Pins
Applying 5 V to a GPIO input can destroy the pin permanently.
The 5 V Pin
That is USB power passing through, not a logic level. Never wire it to a GPIO.
Rule for the whole course
Check the voltage of anything before connecting it to a pin. Damage here is silent and permanent.

## Slide 8
PART 2
Passive Components
A tour, so a schematic stops looking like noise

## Slide 9
Resistors
Lesson 03 | Electrical Fundamentals
9
A resistor limits current. Its value is measured in ohms
The colour bands encode the value, and the code is worth knowing
In practice it is faster and safer to measure it with a multimeter
Surface-mount resistors use a different marking system entirely
Measuring works on every resistor. The colour code does not
Today's practical value
1 kohm. We measure current through it at two different supply voltages.

## Slide 10
LEDs Are Not Resistors
Lesson 03 | Electrical Fundamentals
10
Colour | Forward voltage
Red | 1.8 - 2.0 V
Yellow | 2.0 - 2.2 V
Green | 2.0 - 3.0 V
Blue | 2.8 - 3.2 V
White | 2.8 - 3.4 V
An LED drops a roughly fixed forward voltage
Current must be limited by something else, normally a series resistor
Different colour, different forward voltage, different resistor
A blue LED on 3.3 V leaves almost no headroom for the resistor
On your board
The blue status LED on GPIO 8 already has its resistor fitted. That calculation was done for you.

## Slide 11
An Unconnected Input Is Not Zero
Lesson 03 | Electrical Fundamentals
11
An input pin connected to nothing does not read LOW
It floats, picking up whatever electrical noise is nearby
Read it twice and you may get two different answers
A resistor is what gives a disconnected input a defined value
This is not a rare edge case
Every button, every switch and every unused input on a real board needs a defined level. It is the default job of a pull-up or pull-down.

## Slide 12
Pull-Up and Pull-Down
Lesson 03 | Electrical Fundamentals
12
Pull-Up
Resistor from pin to 3.3 V. Pin reads HIGH at rest. Button connects it to GND, so pressing reads LOW. Active-low logic.
Pull-Down
Resistor from pin to GND. Pin reads LOW at rest. Button connects it to 3.3 V, so pressing reads HIGH. Active-high logic.
The BOOT button on GPIO 9 uses a pull-up
That is why pressing it reads LOW. On the breadboard we build the opposite case so you see both conventions side by side.

## Slide 13
Capacitors and Inductors
Lesson 03 | Electrical Fundamentals
13
Capacitor
Stores charge. Steadies a supply voltage that would otherwise dip whenever the chip draws a burst of current. The small ones next to every chip are decoupling capacitors.
Inductor
Resists changes in current. Found in switching power supplies and filters. Where a capacitor is about storing charge, an inductor is about current and time.
No calculations yet
Today you only need to know these exist and roughly what each is for.

## Slide 14
What a GPIO Pin Can Drive
Lesson 03 | Electrical Fundamentals
14
A GPIO pin is a small switch, not a power supply
It can source or sink only tens of milliamps, and less to stay reliable
Total current across all pins is limited too, not just per pin
Motors, relays and long LED strips need a driver or transistor between
Strapping pins: GPIO 8 and GPIO 9
The chip reads these two pins at power-up to choose a boot mode. Something wired to them can stop the board booting even when your code is perfect. This is why the lesson 02 wiring was left alone. Full treatment in block K4.

## Slide 15
PART 3
Measure, Do Not Assume
Bench supply, your board, and a multimeter

## Slide 16
Using the Multimeter
Lesson 03 | Electrical Fundamentals
16
Voltage
Measured in parallel, across the thing you care about.
Current
Measured in series. Break the circuit and put the meter in the gap.
Resistance
Power off, component disconnected from the rest of the circuit.
The classic way to blow the meter fuse
Meter in current mode, connected across a voltage source. Check the mode and the socket before you connect.

## Slide 17
Ohm's Law on the Bench
Lesson 03 | Electrical Fundamentals
17
Part A - demonstration: one bench supply, one resistor, voltage swept slowly
You see a continuous relationship: double the voltage, double the current
Part B - your turn: your board is the voltage source, 3.3 V pin and 5 V pin
1 kohm on the breadboard, meter in series, record the current at each
Then calculate R = V / I and compare against 1000 ohm
It will not be exactly 1000 ohm
Resistors have a tolerance, commonly 5 percent, and your meter has its own error. This is the first place measuring beats assuming.

## Slide 18
Soldering: Watch Today, Solder Friday
Lesson 03 | Electrical Fundamentals
18
Three soldering stations plus the instructor's own irons
Temperature control, and what flux actually does
A good joint versus a cold joint versus a bridge
The most common real task: header pins onto a board like the Super Mini
Safety
The tip burns instantly and stays hot long after switch off. The iron lives in its holder, never on the bench. Work in ventilated space, do not lean over the fumes, wash hands afterwards.

## Slide 19
Summary
Lesson 03 | Electrical Fundamentals
19
Voltage, current and resistance, and the pipe they behave like
Ohm's law as the tool for choosing a resistor
Resistors, LEDs, pull-ups, capacitors and inductors
What a GPIO pin can drive, and why GPIO 8 and 9 are special
Multimeter: parallel for voltage, series for current, power off for resistance
Homework
Five problems on Ohm's law, resistor selection and power. Paper and a calculator, no hardware. See homework/README.md