## Slide 1
LESSON 05
Variables, Types and Arithmetic
From bits in memory to a temperature on the screen
Embedded Software Development in C/C++
ESP32-C3 Super Mini | Session 5 of 25

## Slide 2
Today
Lesson 05 | Variables, Types and Arithmetic
2
Every value a program uses lives somewhere in memory
A type decides how many bytes that is, and which values fit
Integer arithmetic on a microcontroller follows rules that surprise you
Last hour: a potentiometer on your board, printing a temperature
Goal
By the end of the lesson your board prints a temperature between -40 and +140 F, and you can explain every line of the program that does it.

## Slide 3
PART 1
Memory and Variables
What the board actually stores

## Slide 4
Memory is a row of numbered boxes
Lesson 05 | Variables, Types and Arithmetic
4
Address | Bits in that box | Could mean
0x3FC80000 | 00011001 | the number 25
0x3FC80001 | 01000001 | the number 65, or the letter A
0x3FC80002 | 11111111 | the number 255, or the number -1
The board stores bits. That is all it stores.
The type is the instruction for how to read them.
Same bits, different type, different value.

## Slide 5
A variable has three properties
Lesson 05 | Variables, Types and Arithmetic
5
uint8_t red = 25U;
Name
What you call it in the source. The chip never sees it.
Address
Which box in memory holds the value.
Size
How many boxes it takes. The type decides.
Why size matters here
A laptop has gigabytes of memory. This board has 400 kB in total. Size is not a detail.

## Slide 6
Ask the compiler: sizeof
Lesson 05 | Variables, Types and Arithmetic
6
#include <stdint.h>
uint8_t small = 7U;
uint16_t medium = 7U;
uint32_t large = 7U;
Serial.println(sizeof(small));
Serial.println(sizeof(medium));
Serial.println(sizeof(large));
The same value 7 in all three
Different boxes, different counts
Prints 1, then 2, then 4
Predict the output first, then run it

## Slide 7
PART 2
Types and Their Limits
Every type has an edge, and values fall off it

## Slide 8
The types we use in this course
Lesson 05 | Variables, Types and Arithmetic
8
Type | Bytes | Lowest | Highest
uint8_t | 1 | 0 | 255
int8_t | 1 | -128 | 127
uint16_t | 2 | 0 | 65535
int16_t | 2 | -32768 | 32767
int32_t | 4 | -2147483648 | 2147483647
Reading the names
u means unsigned: zero and upwards, no negative values. The number is how many bits.

## Slide 9
Why not just write int?
Lesson 05 | Variables, Types and Arithmetic
9
int is not the same size everywhere: 4 bytes here, 2 bytes on other chips
uint8_t means exactly one byte, on every machine, forever
Sensor values and hardware registers have fixed widths; your variables should match
Course rule: fixed-width types for anything that touches hardware
Style rule
Unsigned constants carry an explicit suffix: 500U, 3U. It tells both the compiler and the next reader what you meant.

## Slide 10
What happens at the edge
Lesson 05 | Variables, Types and Arithmetic
10
uint8_t counter = 250U;
for (uint8_t i = 0U; i < 8U; i++) {
Serial.println(counter);
counter = counter + 1U;
}
Prints 250 251 252 253 254 255 0 1
No error. No warning. It simply wraps.
int8_t does the same: 120 + 10 gives -126
This is not a bug in C
The type has 256 possible values. After the last one it starts again from the first. Choosing a type means choosing where that edge sits.

## Slide 11
PART 3
Arithmetic That Surprises You
Integer division does not do what school taught

## Slide 12
Integer division cuts
Lesson 05 | Variables, Types and Arithmetic
12
Serial.println(5 / 9); // 0
Serial.println(9 / 5); // 1
Serial.println(-5 / 2); // -2, not -3
There is no fraction to store
The part after the point is dropped
Dropped, not rounded
Negatives cut toward zero too
Where this bites you tonight
The conversion formula contains 5 / 9. Written on its own, that is zero, and the whole result becomes zero with it.

## Slide 13
The order changes the answer
Lesson 05 | Variables, Types and Arithmetic
13
int16_t f = 100;
int16_t a = (f - 32) * 5 / 9; // 37, correct
int16_t b = (f - 32) / 9 * 5; // 35, wrong
Multiply first, divide last
Both compile
Both look reasonable
Nothing warns you
Two points you can check
-40 F is exactly -40 C. 32 F is exactly 0 C. If your program agrees on both, the formula is right.

## Slide 14
Conditions and loops, the short version
Lesson 05 | Variables, Types and Arithmetic
14
if (celsius < 0) {
Serial.println("below freezing");
} else {
Serial.println("above freezing");
}
// loop() is already a forever loop.
// Everything you write there repeats.
== compares, = assigns
The braces hold what runs
You need exactly this much to read tonight's homework

## Slide 15
PART 4
On the Board
Potentiometer, serial monitor, and your homework

## Slide 16
Wiring the potentiometer
Lesson 05 | Variables, Types and Arithmetic
16
Potentiometer pin | Connects to | Note
Middle pin (wiper) | GPIO 4 | Analog input
One outer pin | 3V3 | See the README
Other outer pin | GND | Directly
Three legs go straight into the breadboard. No soldering.
Turning the knob changes the voltage on the middle pin.
If the knob works backwards
Swap the two outer pins. Nothing is damaged, the direction simply reverses.

## Slide 17
The program you are given
Lesson 05 | Variables, Types and Arithmetic
17
// Already written and working:
uint16_t counts = readPotentiometer();
int16_t fahrenheit = mapToFahrenheit(counts);
Serial.print("F = ");
Serial.println(fahrenheit);
// TODO: print the same temperature in Celsius
Reading the knob: done for you
Mapping to Fahrenheit: done for you
The arithmetic: yours
Whole numbers only. No float.

## Slide 18
Summary
Lesson 05 | Variables, Types and Arithmetic
18
Memory holds bits; the type decides how they are read
Fixed-width types make the size and the range visible
Values wrap at the edge of their type, silently
Integer division cuts, and the order of operations changes the result
Homework
Convert the Fahrenheit reading to Celsius using whole-number arithmetic. Check your result at -40 F and at 32 F. Commit and push before the next session.