## Slide 1
LESSON 12
UART on the Pico
Solder the headers, compare three buses, make two boards talk
Embedded Software Development in C/C++
Raspberry Pi Pico (RP2040) | Arduino-Pico core | 2026-10-07
Notes: First session on the Pico. The toolchain was homework, so tonight starts with a short check, then soldering, then buses. Porting the K3 classes is deliberately not tonight.

## Slide 2
Tonight
Lesson 12 | UART on the Pico
2
1
Homework check
2
Solder headers
3
Three buses
4
UART
5
Lab: chat
6
Lab: pot -> blink
Goal for tonight
One Pico reads a potentiometer, the other blinks at the speed it sets - over two wires and a shared ground.
Notes: Rough timing: homework check 10 min, soldering 40, three buses 20, UART theory 30, chat lab 20, protocol lab 50, summary 10.

## Slide 3
PART 1
Homework check
What the first Pico taught us

## Slide 4
Three traps from the first Pico
Lesson 12 | UART on the Pico
4
Upload stops
"picotool was unable to connect" on Windows. Zadig -> RP2 Boot (Interface 1) -> WinUSB. Never touch Interface 0.
LED stays dark
Serial prints, the LED does nothing. pinMode(LED_BUILTIN, OUTPUT) is missing - the pin is not an output yet.
"v2.0" is not Pico 2
INFO_UF2.TXT says v2.0: that is the boot ROM of RP2040 revision B1. The bootloader is in ROM and cannot be updated.
Your pico-setup.md: anything else that bit you?
Notes: Go round the table: one sentence each from pico-setup.md. Problems that more than one person hit go into the homework README for the next stream.

## Slide 5
PART 2
Solder the headers
The breadboard is your jig

## Slide 6
The breadboard is your jig
Lesson 12 | UART on the Pico
6
1
Push both 20-pin headers into the breadboard, long pins down, so the Pico will straddle the centre gap
2
Lay the Pico on top. Check the pins come through every hole
3
Solder one corner pin on each side. Is the board flat? Fix it now, not later
4
Solder the other 38 pins: 350 C, 2-3 s per joint. Matte joints are normal with lead-free solder
5
Let it cool, then lift the Pico out straight
Pico on top
USB end
headers in the breadboard, centre gap between them
Notes: Three stations plus personal irons, four students: two can start at once, the others place headers and check alignment meanwhile. The first two corner pins decide whether the board ends up flat. Do not hold the iron on the breadboard plastic.

## Slide 7
Check before you plug in USB
Lesson 12 | UART on the Pico
7
Look
Every joint with the loupe
A small cone around the pin, no ball, no gap
No bridge between neighbouring pins
Measure
Multimeter on continuity
Neighbouring pins must not beep
GND pins beep with each other: they are one net, that is correct
Then the real test
Plug in USB. Your blink from the homework must still run. If the LED is dark or the board gets warm: unplug and look again.
Notes: Same continuity method as session 4. A bridge between 3V3 and GND would short the regulator, so the check comes before USB, not after.

## Slide 8
PART 3
Three buses
UART, I2C, SPI - one table

## Slide 9
UART vs I2C vs SPI
Lesson 12 | UART on the Pico
9
 | UART | I2C | SPI
Signal wires | TX, RX | SDA, SCL | SCK, MOSI, MISO, CS
Clock | none - agreed baud rate | SCL, from controller | SCK, from controller
Devices | 2, point to point | many, by address | many, one CS each
Direction | both at once | one at a time | both at once
Typical speed | 9600 - 115200 baud | 100 / 400 kHz | 1 - tens of MHz
Outputs | push-pull | open-drain + pull-ups | push-pull
In this course | tonight: board to board | session 13: OPT4001 | session 14: Nokia 5110
Plus GND on every bus: a voltage only means something against a shared reference.
Notes: Do not go deep on I2C and SPI tonight; the table is the map for the next two sessions. Point at the Clock row: UART is the only one without a clock wire, which is why both sides must agree on the speed in advance.

## Slide 10
The Pico pin map for the rest of K4
Lesson 12 | UART on the Pico
10
Function | GPIO | Pin | When
UART0 (Serial1) TX / RX | GP0 / GP1 | 1 / 2 | tonight
On-board LED | GP25 | - | tonight
I2C0 SDA / SCL (OPT4001) | GP4 / GP5 | 6 / 7 | session 13
SPI0 MISO / CS / SCK / MOSI | GP16 / 17 / 18 / 19 | 21 / 22 / 24 / 25 | session 14
Nokia 5110 D/C / RST | GP20 / GP21 | 26 / 27 | session 14
RGB LED R / G / B | GP10 / GP11 / GP12 | 14 / 15 / 16 | later
Buttons A / B | GP14 / GP15 | 19 / 20 | later
Potentiometer (ADC0) | GP26 | 31 | tonight
The buses sit on the Arduino-Pico default pins, so Serial1, Wire and SPI work without setTX() or setSDA().
Notes: GND for the UART wire is physical pin 3, right next to GP0 and GP1. Everything on this map can be wired at the same time - no pin is used twice.

## Slide 11
PART 4
UART
Two wires, no clock

## Slide 12
No clock wire: one byte on the line
Lesson 12 | UART on the Pico
12
HIGH
LOW
idle
start
d0
1
d1
0
d2
0
d3
0
d4
0
d5
0
d6
1
d7
0
stop
idle
'A' = 0x41 = 0100 0001, sent least significant bit first
8N1
8 data bits, No parity, 1 stop bit. The line idles HIGH; the falling edge of the start bit is the only timing reference the receiver gets.
Notes: Read the waveform with them bit by bit. Ask: how does the receiver know where d0 starts? Answer: it sees the falling edge of the start bit and then counts bit times from its own clock. That is why both sides must agree on the baud rate. Session 15 shows exactly this frame on the logic analyzer.

## Slide 13
115200 baud in numbers
Lesson 12 | UART on the Pico
13
115200
bits per second
->
8.68 us
one bit
x
10
bits per byte (8N1)
=
86.8 us
one byte
At most 11520 bytes per second - a full line of text takes a few milliseconds
Both sides count bit times on their own clock. If the two baud rates differ by more than a few percent, the receiver samples the wrong bits
Typical rates: 9600, 115200. Pick one and use it on both boards
Notes: 1 / 115200 = 8.68 us. 10 bits per byte because start and stop are overhead: 20 percent of the line is framing.

## Slide 14
Serial is not Serial1
Lesson 12 | UART on the Pico
14
Serial
USB CDC to your PC. Not a UART at all - the baud rate you pass is ignored.
Serial1
UART0, hardware. GP0 = TX, GP1 = RX. Tonight's wire to your partner.
Serial2
UART1, hardware. Default GP8 = TX, GP9 = RX. Tonight's homework: two UARTs, one board.
Two hardware UARTs
The RP2040 has two UART blocks (ARM PL011) with small FIFOs. The pins can be moved with setTX() / setRX() before begin() - our pin map keeps the defaults.
Notes: Same idea as on the ESP32-C3: what the course called Serial so far was USB all along. Tonight is the first time a real UART pin carries data.

## Slide 15
Wiring two boards
Lesson 12 | UART on the Pico
15
Pico A
Pico B
GP0 TX (pin 1)
(pin 1) TX GP0
GP1 RX (pin 2)
(pin 2) RX GP1
GND (pin 3)
(pin 3) GND
TX goes to RX - crossed
shared ground
Never connect 3V3 or VBUS between the boards. Each Pico is powered by its own USB cable - only GND is shared. 3.3 V logic only: no 5 V, no RS-232.
Notes: Physical pins 1, 2, 3 are next to each other on both boards, so three short jumpers do it. If a pair cannot reach, use the two breadboards side by side.

## Slide 16
The bridge: what you type goes to your partner
Lesson 12 | UART on the Pico
16
static const uint32_t USB_BAUD = 115200U; // ignored by USB
static const uint32_t UART_BAUD = 115200U; // both boards!
void setup() {
Serial.begin(USB_BAUD); // USB to your PC
Serial1.begin(UART_BAUD); // UART0: GP0 TX, GP1 RX
}
void loop() {
while (Serial.available() > 0) { // PC -> partner
Serial1.write(static_cast<uint8_t>(Serial.read()));
}
while (Serial1.available() > 0) { // partner -> PC
Serial.write(static_cast<uint8_t>(Serial1.read()));
}
}
platformio.ini
monitor_speed = 115200
monitor_echo = yes
monitor_filters = send_on_enter
echo: see what you type
send_on_enter: send the whole line on Enter
Lines end with CR LF - remember that for the protocol
Notes: Without send_on_enter the monitor sends every key as you press it; without echo you type blind. monitor_eol defaults to CRLF, so the partner receives text followed by \r\n. The protocol stage has to deal with that.

## Slide 17
PART 5
Lab
Chat first, then a sensor on the line

## Slide 18
Stage 1: chat
Lesson 12 | UART on the Pico
18
1
Pair up: one Pico A, one Pico B
2
Wire TX -> RX, RX <- TX, GND - GND (pins 1, 2, 3)
3
Flash the bridge on both boards, open both monitors
4
Type a line and press Enter: it appears on your partner's screen
5
Pull out one data wire. Which direction stops working - and why only that one?
Nothing arrives?
Check in this order: TX and RX crossed? GND connected? Same baud on both? Monitor open on the right COM port?
Notes: Two pairs. Step 5 answer: each wire carries one direction only - UART is two independent one-way lines.

## Slide 19
Who talks first?
Lesson 12 | UART on the Pico
19
UART has no master: two independent wires, either side may talk at any time. The protocol decides who leads.
Stream
The pot board sends POT 512 every 100 ms on its own. The LED board only listens. Simple - but who notices when it goes quiet?
Poll
The LED board asks POT?, the pot board answers POT 512. The one who needs the data sets the pace.
Command
The pot board works out the period itself and sends PERIOD 300. Should the sensor own that maths?
Which board should lead - and why?
Notes: Let them argue before the next slide. All three are real: GPS modules stream NMEA, I2C sensors are polled, actuators take commands. We pick Poll: the LED board needs the data, so it decides when to ask - and session 13 works exactly like this, with the I2C bus enforcing the roles.

## Slide 20
Stage 2: the LED board leads
Lesson 12 | UART on the Pico
20
Who | Sends | When
LED board (master) | POT? | every 100 ms
Pot board (slave) | POT <0..1023> | only as the answer to POT?
Master: map the value to a blink half-period of 50 .. 500 ms and blink GP25 - no delay()
Master: no answer within 200 ms -> print "no reply", LED off. Back to normal when answers return
Slave: never talks first. Anything other than POT? is ignored
Every message is one line: ends at '\n', '\r' ignored, at most 31 characters
Notes: Pairs: one board is master, one is slave, then swap roles. A reply is about 10 bytes, under 1 ms at 115200, so 200 ms is a generous timeout. The master never sends a new POT? while it is still waiting.

## Slide 21
Wiring the potentiometer (pot board only)
Lesson 12 | UART on the Pico
21
Pico
10k potentiometer
GP26 / ADC0 (pin 31)
middle pin (wiper)
AGND (pin 33)
outer pin
3V3 OUT (pin 36)
other outer pin
No 3.3k resistor this time
On the C3 it worked around the ADC range. The Pico ADC reads the whole 0 .. 3.3 V. analogRead() gives 0 .. 1023 by default (10 bits); analogReadResolution(12) gives 0 .. 4095.
Notes: Pins 31, 33 and 36 sit together near the bottom of the right-hand header. AGND is the ADC's own ground reference; any GND works, AGND is the clean choice. If the value runs backwards, swap the two outer wires.

## Slide 22
Building a line, one byte at a time
Lesson 12 | UART on the Pico
22
static const size_t LINE_MAX = 31U;
static char s_line[LINE_MAX + 1U]; // + 1 for '\0'
static size_t s_len = 0U;
static bool readLine(Stream& in) { // true: s_line is complete
while (in.available() > 0) {
const char c = static_cast<char>(in.read());
if (c == '\r') { continue; } // CR LF -> drop CR
if (c == '\n') {
s_line[s_len] = '\0'; s_len = 0U;
return true;
}
if (s_len < LINE_MAX) { s_line[s_len++] = c; }
}
return false;
}
Bytes arrive one by one, at any time - loop() collects them
A char array from session 7, no String, no heap
Slave: strcmp(s_line, "POT?"). Master: strncmp(s_line, "POT ", 4U), then strtoul() for the number
A cut or garbled line is not a valid reply
Notes: Same function on both boards; both read Serial1. Stream& works for Serial, Serial1 and Serial2 - all derive from Stream. Homework hint for later: one board with two UARTs needs two buffers, which is a good reason for a small LineReader class.

## Slide 23
The master is a state machine
Lesson 12 | UART on the Pico
23
IDLE
blinking at the last period
WAITING
POT? sent, clock running
100 ms since the last POT? / send POT?
reply POT n / new blink period
200 ms, no reply / LED off, print no reply
Fail safe
A LED that keeps blinking after its sensor is gone is lying - silence is information. And roles stop the ping-pong two equal boards can get into: the slave never talks first, the master never answers.
Notes: enum class MasterState { Idle, Waiting } and a switch, exactly as in K3. The blink runs independently of both states, driven by millis(). Discussion: should one missed reply already switch the LED off, or three in a row? Real links (an RC transmitter, for example) count several misses before they declare failsafe.

## Slide 24
Summary
Lesson 12 | UART on the Pico
24
Headers soldered, checked by eye and by continuity before power
UART: no clock wire, both sides agree on the baud rate. 8N1 = 10 bits per byte
Serial is USB; Serial1 = UART0 (GP0 / GP1); Serial2 = UART1 (GP8 / GP9)
TX to RX crossed, GND shared, never 3V3 or VBUS between boards
The protocol decides the roles: the master asks, the slave answers, silence means fail safe
Homework
One Pico, two UARTs: the pot side answers on UART0, the LED side asks on UART1. Wires GP0 -> GP9 and GP8 -> GP1. Task in homework/README.md.
Notes: Everyone leaves with a soldered, tested board. Session 13 adds the OPT4001 light sensor on I2C (GP4 / GP5) - the same master/slave idea, this time enforced by the bus.