## Slide 1
LESSON 16 | OPTIONAL BLOCK S1
STM32: CubeMX and HAL
Black Pill F411, USB DFU upload, two I2C sensors
Embedded Software Development in C/C++
Session 16 | 4 academic hours
Notes: Timing (4 x 45 min): install check 20 min, board and layers 15, CubeMX 40, build and DFU 30, HAL GPIO and USB log 25, I2C sensors 40, lab the rest. Three Black Pills: work in pairs, instructor board for the demo.

## Slide 2
Today
Lesson 16 | STM32: CubeMX and HAL
2
A new board with no Arduino layer: STM32F411 Black Pill
CubeMX: pins, clock tree, peripherals -> generated C project
Build in VS Code, upload over USB with the ROM bootloader (DFU)
HAL in polling mode: GPIO, USB virtual COM port, I2C
Two new sensors: MPU-6050 (register based) and BH1750 (command based)
Check the I2C traffic with PulseView, as in session 15
Before we start
VS Code STM32 extension, CubeMX with the F4 package, CubeProgrammer. Missing something? Start the download now.
Notes: Install check first. Anyone without the F4 package in CubeMX: start it now, it is the longest download.

## Slide 3
PART 1
A New Board
What changes when Arduino is gone

## Slide 4
Pico vs Black Pill
Lesson 16 | STM32: CubeMX and HAL
4
 | Raspberry Pi Pico | Black Pill
MCU | RP2040 | STM32F411CEU6
Core | 2 x Cortex-M0+ | 1 x Cortex-M4F (FPU, DSP)
Clock | 133 MHz | up to 100 MHz (96 today)
Flash / RAM | 2 MB external / 264 KB | 512 KB internal / 128 KB
Upload | UF2 drive (BOOTSEL) | USB DFU (BOOT0) or SWD probe
Framework | Arduino-Pico | CubeMX + HAL (plain C)
Crystal | 12 MHz | 25 MHz (HSE)
Notes: Both are Cortex-M, so registers like NVIC and SysTick are the same family. The F411 has an FPU: float math is cheap here, unlike on the M0+.

## Slide 5
Black Pill: What We Use Today
Lesson 16 | STM32: CubeMX and HAL
5
Function | Pin | Notes
LED (blue) | PC13 | Active low: RESET = on. Weak pin, max 3 mA
KEY button | PA0 | To GND, needs the internal pull-up
BOOT0 / NRST | buttons | Enter the ROM bootloader (DFU)
USB-C | PA11 / PA12 | USB OTG FS: DFU and our COM port
I2C1 SCL / SDA | PB6 / PB7 | Both sensors on one bus
Sensor power | 3V3, GND | Never 5V on the I2C lines
No ST-Link on this board
Upload works over USB. Breakpoints need an external SWD probe - later in the block.

## Slide 6
Same LED, Three Layers
Lesson 16 | STM32: CubeMX and HAL
6
// Arduino (what we used so far)
digitalWrite(LED_PIN, LOW);
// HAL (today): port + pin + state
HAL_GPIO_WritePin(GPIOC, GPIO_PIN_13, GPIO_PIN_RESET);
// Register: one write to the bit set / reset register
GPIOC->BSRR = GPIO_BSRR_BR13; // BR = reset bit 13
HAL = ST's C library on top of the registers, one per chip family
No setup(), no pinMode(): CubeMX writes the init code for us
Notes: Ask: which line is fastest? Which is portable to an ESP32? None of them is portable across vendors - that is the Z1 topic.

## Slide 7
The Tool Chain
Lesson 16 | STM32: CubeMX and HAL
7
CubeMX
Pins, clocks, peripherals. Generates a CMake project
->
VS Code
STM32 extension: compiler, CMake, Ninja. Builds the .elf
->
CubeProgrammer
Writes the .elf to flash over USB DFU
->
Board
Press NRST, the program starts
PlatformIO did all four steps with one button. Now each step is visible
Since CubeIDE 2.0, CubeMX is a separate program even for CubeIDE users

## Slide 8
PART 2
CubeMX
From an empty chip to a generated project

## Slide 9
CubeMX: Pinout and Peripherals
Lesson 16 | STM32: CubeMX and HAL
9
Where | Setting
New project | MCU selector: STM32F411CEUx
System Core -> RCC | HSE: Crystal/Ceramic Resonator
System Core -> SYS | Debug: Serial Wire (keeps SWD usable)
PC13 | GPIO_Output, label LED, output level High
PA0 | GPIO_Input, label KEY, Pull-up
Connectivity -> I2C1 | I2C, 100 kHz -> lands on PB6 / PB7
Connectivity -> USB_OTG_FS | Mode: Device_Only
Middleware -> USB_DEVICE | Class: Communication Device Class (CDC)
Notes: Labels matter: LED and KEY become LED_Pin / LED_GPIO_Port in main.h. Check that I2C1 really landed on PB6/PB7 (it may pick PB8/PB9 - click the pin and choose). Output level High = LED off at reset, because the LED is active low.

## Slide 10
Clock Tree: Why 96 MHz, Not 100
Lesson 16 | STM32: CubeMX and HAL
10
Step | Value | Result
HSE crystal | 25 MHz | 25 MHz
/ M | 25 | 1 MHz into the PLL
x N | 192 | 192 MHz (VCO)
/ P -> SYSCLK | 2 | 96 MHz
/ Q -> USB | 4 | 48 MHz, exactly
APB1 / APB2 | /2, /1 | 48 MHz (max 50), 96 MHz
USB needs exactly 48 MHz
100 MHz SYSCLK leaves no Q that gives 48
HSI (16 MHz RC) is not accurate enough for USB: use the crystal
Try it: type 100 into HCLK and watch the USB box turn red
Notes: In CubeMX: Clock Configuration tab, PLL Source Mux = HSE, type 96 into HCLK and press Enter - the solver finds M/N/P/Q. Then show 100 failing.

## Slide 11
Generate Code - and the USER CODE Rule
Lesson 16 | STM32: CubeMX and HAL
11
Project Manager: name lesson16, Toolchain / IDE = CMake
Generate Code writes main.c, startup, HAL, USB middleware, CMakeLists
Regenerate after every change in CubeMX - it rewrites the files
/* USER CODE BEGIN 2 */
app_init(); // survives Generate Code
/* USER CODE END 2 */
HAL_Delay(10); // outside the markers: DELETED next time
Only code between BEGIN and END survives
Our approach: all our code in app.c, main.c gets two calls only.

## Slide 12
PART 3
Build and Upload
VS Code, then the ROM bootloader

## Slide 13
Build in VS Code
Lesson 16 | STM32: CubeMX and HAL
13
STM32 panel -> import the generated folder as a CMake project
Add our file to the root CMakeLists.txt, then Build
Result: build/Debug/lesson16.elf
# CMakeLists.txt (root) - generated, this block is ours
target_sources(${CMAKE_PROJECT_NAME} PRIVATE
# Add user sources here
Core/Src/app.c
)
Linker summary
The build prints FLASH and RAM usage. Compare with the 512 KB / 128 KB from the table.
Notes: Button names differ slightly between extension versions. The CMake: Build command (F7) always works.

## Slide 14
Upload over USB: DFU
Lesson 16 | STM32: CubeMX and HAL
14
1. Enter DFU
Hold BOOT0, press and release NRST, release BOOT0. LED stays dark.
2. Connect
CubeProgrammer: USB, refresh, port USB1, Connect
3. Program
Erasing and Programming: choose the .elf, Start Programming
4. Run
Disconnect, press NRST. Our code starts
The DFU bootloader lives in ROM (system memory): it cannot be erased by mistake
Not found? Data cable, repeat step 1, on Windows reinstall CubeProgrammer drivers
Notes: BOOT0 sampled at reset selects system memory instead of flash. Holding BOOT0 while plugging in works too, but the NRST sequence is more reliable on these boards.

## Slide 15
PART 4
HAL in Our Code
GPIO and the USB virtual COM port

## Slide 16
GPIO and Time with HAL
Lesson 16 | STM32: CubeMX and HAL
16
static const uint32_t BLINK_MS = 500U;
static uint32_t last_ms = 0U;
void app_loop(void)
{
const uint32_t now = HAL_GetTick(); // like millis()
if ((now - last_ms) >= BLINK_MS) {
last_ms += BLINK_MS;
HAL_GPIO_TogglePin(LED_GPIO_Port, LED_Pin);
}
GPIO_PinState key = HAL_GPIO_ReadPin(KEY_GPIO_Port, KEY_Pin);
if (key == GPIO_PIN_RESET) { /* pressed: active low */ }
}
HAL_GetTick(): ms since reset, SysTick, same as millis()
LED_Pin, LED_GPIO_Port: from our CubeMX label
Same non-blocking pattern as in K3
No pinMode(): MX_GPIO_Init() did that

## Slide 17
A printf over USB
Lesson 16 | STM32: CubeMX and HAL
17
static void log_printf(const char *fmt, ...)
{
static char buf[LOG_BUF_SIZE]; // USB reads it later
if (!cdc_wait_idle(CDC_TIMEOUT_MS)) { return; } // nobody reads
va_list args;
va_start(args, fmt);
int len = vsnprintf(buf, sizeof buf, fmt, args);
va_end(args);
if (len > 0) {
CDC_Transmit_FS((uint8_t *)buf, (uint16_t)len);
}
}
CDC_Transmit_FS() only starts a transfer
Wait for the previous one before writing buf again
No %f: newlib-nano printf has no floats. Use tenths
Baud rate in the terminal is ignored
Notes: Simplified for the slide - full version with length clamping in demo/Core/Src/app.c. cdc_wait_idle() checks hUsbDeviceFS.dev_state and the TxState of the CDC handle. Before the host has configured the device the handle is NULL - printing in app_init() would be lost, that is why the demo waits. Terminal: pio device monitor, or any serial monitor; the port is /dev/cu.usbmodem... on macOS, COMx on Windows.

## Slide 18
PART 5
I2C with HAL
GY-521 (MPU-6050) and BH1750

## Slide 19
Wiring and the Address Trap
Lesson 16 | STM32: CubeMX and HAL
19
Module pin | GY-521 | BH1750 | Black Pill
VCC | VCC | VCC | 3V3
GND | GND | GND | GND
SCL | SCL | SCL | PB6
SDA | SDA | SDA | PB7
Address pin | AD0 -> GND: 0x68 | ADDR -> GND: 0x23 | -
// HAL wants the 7-bit address shifted left by one
static const uint16_t MPU_ADDR = (uint16_t)(0x68U << 1);
Forget the shift and every call returns HAL_ERROR
Arduino Wire shifts for you. HAL does not. Scan with HAL_I2C_IsDeviceReady(&hi2c1, a << 1, ...)

## Slide 20
MPU-6050: Register Based
Lesson 16 | STM32: CubeMX and HAL
20
uint8_t who = 0U;
HAL_I2C_Mem_Read(&hi2c1, MPU_ADDR, 0x75U, // WHO_AM_I
I2C_MEMADD_SIZE_8BIT, &who, 1U, 10U);
uint8_t wake = 0x00U; // clear SLEEP
HAL_I2C_Mem_Write(&hi2c1, MPU_ADDR, 0x6BU, // PWR_MGMT_1
I2C_MEMADD_SIZE_8BIT, &wake, 1U, 10U);
uint8_t b[14]; // ax ay az temp gx gy gz, big endian
HAL_I2C_Mem_Read(&hi2c1, MPU_ADDR, 0x3BU, // ACCEL_XOUT_H
I2C_MEMADD_SIZE_8BIT, b, 14U, 10U);
Clones
Many GY-521 boards carry a clone chip: WHO_AM_I 0x70, 0x72 or 0x98 instead of 0x68. Print the value, do not hard-fail.
Notes: Numbers are inline for the slide; the demo uses named constants. Scaling at +-2 g: 16384 LSB per g, so mg = raw * 1000 / 16384. Temperature: raw / 340 + 36.53 C. One Mem_Read = write register, repeated START, read.

## Slide 21
BH1750: Command Based
Lesson 16 | STM32: CubeMX and HAL
21
uint8_t cmd = 0x01U; // power on
HAL_I2C_Master_Transmit(&hi2c1, BH_ADDR, &cmd, 1U, 10U);
cmd = 0x10U; // continuous, 1 lx
HAL_I2C_Master_Transmit(&hi2c1, BH_ADDR, &cmd, 1U, 10U);
uint8_t b[2]; // every >= 180 ms
HAL_I2C_Master_Receive(&hi2c1, BH_ADDR, b, 2U, 10U);
uint32_t raw = ((uint32_t)b[0] << 8) | b[1];
uint32_t lux10 = raw * 25U / 3U; // lux = raw / 1.2
 | Register based (MPU-6050) | Command based (BH1750, AHT10)
Write | register address, then data | a command byte
Read | HAL_I2C_Mem_Read() | HAL_I2C_Master_Receive()

## Slide 22
Check It on the Wire
Lesson 16 | STM32: CubeMX and HAL
22
D1 SDA = PB7, D2 SCL = PB6, GND to GND. I2C decoder, as in session 15
Sample at 1-2 MHz: 100 kHz bus, 10-20 samples per bit
Find the MPU burst: Write 0x68, 0x3B, repeated START, Read 0x68, 14 bytes
Find the BH1750 read: Read 0x23, 2 bytes, no register byte
Unplug a sensor: what does the NACK look like, what does HAL return?
Same bus, different chip
The waveform does not care whether Arduino Wire or HAL produced it. The logic analyzer is the neutral judge.

## Slide 23
Lab (in pairs)
Lesson 16 | STM32: CubeMX and HAL
23
1. Your own CubeMX project from the settings on slides 9-10, generated as CMake
2. Blink the LED with HAL_GetTick(), upload with DFU
3. KEY changes the blink period
4. log_printf over USB: print the SYSCLK with HAL_RCC_GetSysClockFreq()
5. I2C scan: both 0x23 and 0x68 must show up
6. Read WHO_AM_I, then lux. Stretch: acceleration in mg
Stuck?
Check the order: clock tree -> USB enumerates -> terminal open -> I2C. Do not debug two at once.
Notes: Pairs: three Black Pills. The full demo (app.c) is shown at the end, not handed out before the lab.

## Slide 24
Summary
Lesson 16 | STM32: CubeMX and HAL
24
CubeMX generates init code; our code lives in USER CODE sections and app.c
The clock tree is a design decision: USB forced 96 MHz
DFU: the ROM bootloader, entered with BOOT0 + NRST
HAL calls are explicit: port and pin, handle, timeout, return status
I2C: address << 1, Mem_Read for registers, Master_Receive for commands
Keep your project
The next STM32 session builds on the same CubeMX project and board.